Apollo-3 BLE communication between Apollo3 boards

# 1. Foreword

As part of a project to better understand Bluetooth, I have worked connecting boards from Sparkfun based on Apollo3. The connection is using the lightweight, propriety AMD Transaction Protocol, or AMDTP

The Apollo3 board is acting as a server and all actions are initiated by a client running on another Apollo3 board. The client has also been tested to run on with IDE 1.8.12.

An example BLE_led was available, but only provides the functionality to put a led on and off. Not very helpful. This solution can do MUCH more to exchange data.

A separate client version based on Linux (Ubuntu or Raspberry Pi) is also available on https://github.com/paulvha/apollo3/tree/master/ble_amdtp_raspPi

Paul van Haastrecht
paulvha@hotmail.com

Version 1.0 / March 2020
 * initial version

Version 2.0 / March 2020

  * updated to handle security / hashing (auto detect)
  * added major/minor version number request/response
  * update to sent float number for temperature values and battery level
  * changed names of some files
  * changed the internal temperature calculation

# 2. Hardware

## 2.1 Server board

The server software has been tested on a Redboard Artemis ATP (DEV-15442) and a Sparkfun Edge Development board (DEV-15170). On the later, not all pins are available, actually NONE of the ADC pins is available. So it is better to have the ATP run as server.

Optionally an BME280 can be connected on both leveraging the QWIIC interface, or use the SDA / SCL connectors on the ATP. The Adafruit BME280 has been tested successfully, but others could be used as well. You would need to make sure however that the I2C address is correctly set.

## 2.2 Client hardware

The client software has been tested on a Redboard Artemis ATP (DEV-15442) and a Sparkfun Edge Development board (DEV-15170).

# 3. Software installation

## 3.1 Server software
### 3.1.1 Apollo3 software

Make sure you have the latest Apollo3 Arduino library. At the time of testing that was 1.0.30. Follow the steps on https://learn.sparkfun.com/tutorials/artemis-development-with-arduino?_ga=2.21301179.126288810.1581865370-203897739.1571077629

Select the right board in the Arduino IDE.

### 3.1.2 Application software

Select the folder with the amdtps.ino. This folder contains other files that are necessary for compiling.

Parts of the code are coming from Sparkfun BME280 library, which you need to include for BME280: https://github.com/sparkfun/SparkFun_BME280_Arduino_Library

Make the optional changes in the top of the amdtps.ino as defined in chapter 4.1.2.

Now compile and load the software to the board. On the Edge board you will have to manually set it in bootloader :

press and hold reset
press and hold button 14
release reset, while holding button 14

Once it starts uploading you can release button 14. After upload it might be necessary to press reset to start the program.

## 3.2 Client software

### 3.2.1 Apollo3 software

Make sure you have the latest Arduino library. Follow the steps on https://learn.sparkfun.com/tutorials/artemis-development-with-arduino?_ga=2.21301179.126288810.1581865370-203897739.1571077629

Select the right board in the Arduino IDE.

### 3.2.2 Client Application software

Select the folder with the amdtpc.ino. This folder contains other files that are necessary for compiling.

Make the optional changes to the client software see chapter 4.2.2.

Now compile and load the software to the board. On the Edge board you will have to manually set it in bootloader :

press and hold reset
press and hold button 14
release reset, while holding button 14

Once it starts uploading you can release button 14. After upload it might be necessary to press reset to start the program.

# 4. Software overview

## 4.1 Server Software

The server solution has been build with the Arduino Apollo3 software as created by Sparkfun. This software (1.0.30) is based on the Ambiqsuite SDK for the Apollo3. The AMD Transfer Protocol (AMDTP) has been taken from the Ambiqsuite and for the base for the sketch the Sparkfun provided example8_BLE_LED.ino. The server support (optional) an BME280, for which the software has been taken from Sparkfun BME280 library. Make sure to include the library (see 3.1.2)

This software has also been tested by applying with the EXACTLE stack ported from Ambiq SDK 2.3.2 (which supports hashing). The software will auto-detect this option and adjust.

### 4.1.1 High level overview

The core components are the EXACTLE Bluetooth stack, also known as CORDIO stack, which is part of the board package. The AMD transfer protocol, which is included as part of the additional file in the amdtps directory (same as the .ino). Once initialized the server will wait for a client to connect and receiving data. With any data received it will call UserRequestReceived() in the sketch to handle the request on user level. Once completed the user will call SendReplyClient() with the data to return.

The format of the data is:
val[0] = requested command sent by Client, now returned to client
val[1] = length of any optional additional data (else 0)
val[2] = start of optional additional data

The format of the additional data is free form, maximum 100 characters. (see 4.1.2) It is the responsibility of the user to make sure Server and Client know how to interpret the data depending on the requested command.

NOTE: if the execution of a command too long, the Bluetooth stack might get stuck. See example of ‘chat’ how to overcome that.

### 4.1.2 Parameter setting

A number of parameters can be changed in the top of the sketch amdtps.ino

#define BLE_PERIPHERAL_NAME "Artemis AMDTP BLE"
This defines the name of the server as it will show on Bluetooth.

#define MAXREPLY 100
Defines the maximum buffer length of data that can be submitted

#define TempOffset -0.1241
Correction on the internal temperature measurement. See chapter 6 for in-depth explanation.

#define INCLUDE_BME280
This enables including the BME280 software in the server. Default it is commented out.

ONLY VALID IF BME280 is selected
bool ALTM = true; sent Altitude in meters (true) or feet (false)
  bool TEMPC = true; sent temperature in Celsius (true) or Fahrenheit (false)

For DEBUG the following options are available, which are disabled by default. These need to be set in the additional file debug.h:

#define BLE_Debug will show all the data and program flow
#define BLE_SHOW_DATA will only show the data received and sent

In amdtps.ino the server version numbers are defined:

#define MAJOR_SERVERVERSION 2
// new features implemented that require update to client
#define MINOR_SERVERVERSION 0
// bug fixes, better calculation / layout
## 4.2 Client Software

The client solution has been build with the Arduino Apollo3 software as created by Sparkfun. This software (1.0.30) is based on the Ambiqsuite SDK for the Apollo3. The AMD Transfer Protocol (AMDTP) has been taken from the Ambiqsuite and for the base for the sketch the Ambiq Freetos amdtpc software was taken.

This software has also been tested by applying with the EXACTLE stack ported from Ambiq SDK 2.3.2 (which supports hashing). The software will auto-detect this option and adjust .

### 4.2.1 High level overview

The core components are the EXACTLE Bluetooth stack, also known as CORDIO stack, which is part of the board package. The AMD transfer protocol, which is included as part of the additional file in the amdtpc directory (same as the .ino).

Once initialized the client will show a 3 option menu: GAP, GATT and AMDTP.
- The first action is to scan for devices in the GAP menu (option 1).
- Once devices has been found, select Create connection (option 4) and select the devices index-number connect.
- Once connected, it will return to the main menu.

Now select the AMDTP menu to interact with the server user interface (UI) commands.

### 4.2.2 Parameter setting

The parameters are combined in the file ‘ble_menu.h’

// version number
#define MAJOR_CLIENTVERSION 2
// new features implemented that require update to client
#define MINOR_CLIENTVERSION 0
// bug fixes, better calculation/ layout

//#define AM_DEBUG_PRINTF
This enables extended debug messages across all the files of the client solution. In the top of each file this is translated to enable debug messages for that specific file. That might be handy if you focus on debugging only part of the file. (commented out by default)

#define BLE_MENU
Will enable the menu approach, in case later files should be used for other reasons.

#define AM_MENU_BUFSIZE 256
The buffer to display menu strings with am_menu_printf().

#define RXDATALEN 50
Maximum data length from keyboard input.

# 5. Client Menu selection
## 5.1 Main menu
--------------BLE main menu--------------------
1. BLE_MENU_ID_GAP
2. BLE_MENU_ID_GATT
3. BLE_MENU_ID_AMDTP
hint: use 'h' to do main menu
 -----------------------------------------------------
The main menu has 3 options.

## 5.2 GAP menu
----------------------GAP menu----------------------
1. Start Scan
2. Stop Scan
3. Show Scan Results
4. Create Connection
5. Close connection
6. Toggle Through-put measurement

hint: use 'h' to do main menu
-----------------------------------------------------

1. Start scan :
will start the scanning process for other Bluetooth devices. Will time out after 4 seconds

2. Stop scan :
Manually stop scanning.

3. Show Scan result :
Will show an overview of the detected devices during scan.

--------------------Scan Results--------------------
0 : 0 66:77:88:23:BB:EF Artemis AMDTP BLE
----------------------------------------------------- ----
Where :
‘0 :’ is the index number
‘0’ is the address type defined as :

HCI_ADDR_TYPE_PUBLIC 0 /*!< \brief Public device address */
HCI_ADDR_TYPE_RANDOM 1 /*!< \brief Random device address */
HCI_ADDR_TYPE_PUBLIC_IDENTITY 2 /*!< \brief Public identity address */
HCI_ADDR_TYPE_RANDOM_IDENTITY 3 /*!< \brief Random identity address */
HCI_ADDR_TYPE_ANONYMOUS 0xFF /*!< \brief Anonymous device address */

‘66:77:88:23:BB:EF’ : the Bluetooth address

‘Artemis AMDTP BLE’ : name provided by the detected Bluetooth devices (if correctly detected)

4. Create connection:
Will show the detected devices as mentioned above and now select the index number of the device to connect of press ‘h’ to return to main menu.

5. Close device :
Will close a current connection.

6. Toggle through-put measurement :
This will provide on regular interval the amount of bytes that have been received.

## 5.3 GATT menu
At this stage the GATT menu does not have any options to select.

## 5.4 AMDTP menu
Once connected the main menu will be show again and now selected option 3.

----------------------AMDTP menu----------------------
1. Request Server to send test data
2. Request Server to stop sending test data
3. Sent ‘Hello’ to server
4. Request battery level percentage
5. Request battery level percentage with load resistor
6. Request internal temperature in Celsius
7. Request internal temperature in Fahrenheit
8. Turn server onboard led on
9. Turn server onboard led off
10. Request BME280 measurement
11. Request ADC pin level
12. Request chat session
13. Request digital pin level
14. Set digital pin High
15. Set digital pin Low
30. Request Server version number

hint: use 'h' to do main menu
-----------------------------------------------------

1. Start receiving test data
Entering 1<enter> the server will sent “test #” every second or so. The # will increment with each received message.

2. Stop receiving test data
Entering a 2 <enter> will instruct the server to stop sending test data. The menu will reappear.

3. Send hello
Just a test to check the connection is working. The server will reply with an “Hello” responds. The menu will reappear.

4. Battery level in percentage
The Apollo3 processor has an internal ADC sensor for the battery level, no additional hardware needed. This option will display the percentage of measured value / 3.3V (which is the expected voltage). Too high or TOO low can cause issues. The menu will reappear.

5. Battery level in percentage with load resistor
The Apollo3 processor has an internal ADC sensor for the battery level AND an internal load resistor ( ~500 ohm), no additional hardware needed. This option will display the percentage of measured value / 3.3V (which is the expected voltage). By first setting the resistor and then measure the percentage you get an impression about the quality of the supply under load. After measurement the resistor is removed. Much lower value than measure without load resistor can indicate weak power supply. The menu will reappear.

6 & 7 Read internal temperature in Celsius /Fahrenheit
The Apollo3 processor has an internal temperature measurement, no additional hardware needed. This option will display in Celsius or Fahrenheit that internal temperature and the menu will reappear. See chapter 6 for more detail about internal temperature measurement.

8. Turn LED on
Will turn ON the on-board led on the server. The menu will reappear.

9. Turn LED off
Will turn OFF the on-board led on the server. The menu will reappear.

10. Read BME280 (if connected)
Optionally a BME280 can be connected to the server. This must be enabled in the sketch, see chapter 4.1.2 as well info in top of sketch. If enabled this will show the BME280 result. The menu will reappear.

11. Read ADC channel
After selecting this option you need to provide a valid ADC channel of the Apollo3 to be read. The results will be between 0 and 1023 and in volt. The menu will reappear.

12. Perform simple chat
This will allow to sent a line of text (max 45 characters) taken from the keyboard from the client to the server. It will wait for the server to respond, but not endless. The message will be displayed on the server and what is typed on the server is displayed at the client. If the server or the client is sending BYE, the connection will close and the menu will re-appear.

13. Read a digital pin
After selecting this option you need to provide a valid digital pin of the Apollo3 to be read. The result will be HIGH or LOW. The menu will reappear.

14 & 15 Set a pin HIGH or LOW
After selecting this option you need to provide a valid digital pin of the Apollo3 to be set. The menu will reappear.

30. Request Server version number
Will request and display the server and client version number. The consists of a MAJOR and MINOR number (e.g. 2.1). The MAJOR number should stay in sync with the client MAJOR number as this will change whenever new features OR changes are applied that impact both server and client. The Minor number is bug-fixing, display changes or calculation changes that impact only the server or the client.

# 6 Internal Temperature adjustment

The Apollo3 has an internal temperature sensor that can be read with the ADC circuit. According to the datasheet it has a sensitivity of 3.8mV/degree and +/- 3 ºC. (datasheet page 782)

## 6.1. Original approach

The Apollo3 chip can be calibrated in the factory to have an optimal reading of the internal temperature sensor. These calibration parameters are then stored in the Apollo3 chip. When initializing the ADC circuit, the SDK tries to read these calibration values.. If these values are NOT set (all 0xfffffff), it will apply the following default values:

In am_hal_anlog.h :
  // ***************************************************************************
  //
  // Default coefficients (used when trims not provided):
  // TEMP_DEFAULT = Temperature in deg K (e.g. 299.5 - 273.15 = 26.35)
  // AMBIENT_DEFAULT = Voltage measurement at default temperature.
  // OFFSET_DEFAULT = Default ADC offset at 1v.
  //
  // ***************************************************************************
  #define AM_HAL_ADC_CALIB_TEMP_DEFAULT (299.5F)
  #define AM_HAL_ADC_CALIB_AMBIENT_DEFAULT (1.02809F)
  #define AM_HAL_ADC_CALIB_ADC_OFFSET_DEFAULT (-0.004281F)

In am_hal_analog.c :
  // Since the device has not been calibrated on the tester, we'll load default calibration values.
  // These default values should result in worst-case temperature measurements of +-6 degrees C.

### 6.2.1 What does that mean ?
It assumes that the sensor at a temperature of 26.35 ºC an ADC calculated voltage provides of 1.02809 volt. The ADC has an offset error to a perfect ADC line of -0.004281 (changes the measured value later). This is a slope that has higher impact on the lower number than a larger number (higher temperature). With these default number the accuracy would be dropping from +/- 3 ºC to +/- 6 ºC.

### 6.2.2 Reality check
I have 3 boards, 2 x Edge + ATP. Only the ATP contains an Apollo3 with calibrated data. The test program (6.4) will provide information whether the Apollo3 chip contains calibrated internal temperature sensor data or not. When using the original calculation in the SDK, one Edge board was about 1 degree off, and the other about 5 degrees. While within the 6 degrees, the alternative approach might be better for server boards with that contains an Apollo3 that does NOT contain calibration data for the internal temperature sensor.

## 6.3 Alternative approach
We have taken a different approach: We do not know the ADC offset per Apollo3, we do not know the temperature sensor linearity or slope . Only default numbers as an estimate for correction that does not provide usable results for one board

The approach is as follows
- Measure the BME280 temperature (temp Celsius -> temp Kelvin)
- Translate that to an expected ADC voltage (V(BME280) = temp in Kelvin * 3.8mV)
- Measure the internal temperature sensor ADC in 14 bits. (ADC)
- Translate that to the voltage (V(ADC) = ADC * 2 / 16384.0F);
- Now take the delta between the 2 voltages (D = V(bme280) - V(ADC))

Have a test program run for longer time and noted down that delta:
Edge	-0.1146
edge1	-0.1241

Then I applied the correction factor to the v(ADC).

I do not have a lab-environment so I have done the tests at a temperature of 24.8 degrees Celsius. Then I warmed the BME280 and board it up op ~37 degrees... the delta between the internal sensor and BME280 was < 0.7 degrees......

So while there is a slope and ADC offset, if the result is within +/- 1 degree on a range of 15 to 35 degree Celsius compared to 25 degree, I consider that good enough. Better than applying the default values in that case. It is not a medical solution 🙂

## 6.4 Test program AdcTemp

A test program, AdcTemp, is in the extra-folder of the amdtps package. This program will require a BME280 or BM680 to perform the following activities.
1. Test whether the Apollo3 chip on your board has calibrated data for the temperature sensor.
2. If it has calibrated data it will display the temperature from the internal an external sensor
3. If it does not have calibrate data, it will follow the steps in the approach as defined in 6.3

The following output will be seen in case it is NOT calibrated (done with BME280):

Temperature correction detection. Compiled: 22:37:16

TRIMMED TEMP = 299.500000
TRIMMED VOLTAGE = 1.028090
TRIMMED Offset = -0.004281
Note - these trim values are 'un-calibrated default' values.

------ Internal sensor----- -------BME280 ------- --- adjustment -- ----- adjusted ------
  org Temp voltage Temperature voltage calculated applied Temperature
  20.25	1.0071	22.13	1.1221	-0.1150	-0.1234	24.34
  20.40	1.0076	22.15	1.1221	-0.1146	-0.1234	24.47
  20.43	1.0077	22.15	1.1221	-0.1144	-0.1234	24.51
  20.15	1.0067	22.15	1.1221	-0.1154	-0.1234	24.25
  20.11	1.0066	22.15	1.1221	-0.1155	-0.1234	24.22

It will first display the Apollo3 trim-data and indicate whether these are taken from the Apollo3 chip, and as such calibrated, or default data, as such un-calibrated. It UN-calibrated it will show the columns as above.

Column 1: org.temp
This is the temperature based on the measured ADC value from the internal sensor
Column2 : voltage
The corresponding calculated voltage based on the measured ADC value.
Column3 : Temperature
The external sensor measured value.
Column 4 : voltage
The corresponding calculated voltage based on the measured external temperature.
Column 5 : adjustment calculated
The delta between the external sensor voltage and internal sensor voltage
Column 6 : applied
The offset voltage provided in the top of the sketch to test impact
Column 7: Temperature
The temperature based on the ADC measurement + the applied offset

### 6.4.1 Required libraries

The BME280 requires :https://github.com/sparkfun/SparkFun_BME280_Arduino_Library
The BME680 requires: https://github.com/adafruit/Adafruit_BME680

### 6.4.2 How to use?

Start by running the program as it as.

The BME280 is selected by default as the external sensor, but you can select a BME680 instead on line 50 / 51. Only selected either of them.
When the program indicates that the Apollo3 chip for the server board has calibrated data for the internal sensor, you are done. All it will show is the internal sensor temperature and external sensor temperature.

If un-calibrated, let the program run for some time (minute). Ideally in an environment that is close the expected operating temperature, normally around 25 degrees Celsius, and a bit stable

Observe column 1: org. temp and compare against column3 BME280 Temperature. If the values are close (< 2 or 3 degrees), you can use the default un-calibrated values. You are done.

Else

1. observe column 5 : adjustment calculated.
2. The number will fluctuate a little and try to detect a value to that you see most of the time.
3. Stop the program and in the top of the sketch (line 57) now apply that value in :
float TempOffset = -0.1234; (WATCH + OR - !!)
1. Recompile, load and run the sketch.
2. You should see the applied value column 6 and the adjusted temperature in column 7.
3. Compare Column 3: BME280 temperature to Column 7. If you are happy with the result, you are done, else observe coun5 and repeat the steps 1 – 5.

Once done write down the applied value. MAKE GOOD NOTICE WHETHER IT IS A POSITIVE OR NEGATIVE NUMBER !!

## 6.5 Update in amdtps

If the Apollo3 chip for the server board has calibrated data, there is nothing more you need to do.

If the Apollo3 chip does not have calibrated data

1. If you are OK with using the default values, leave unchanged (around line 98)
#define TempOffset 0

2. If you want to apply a correction value, set (around line 98)
#define TempOffset 0 to #define TempOffset <applied value>
    As you set the value, make sure to add the minus sign if applicable.
# Appendix A : Adding an option

This describes the different steps to take to add an option between client and server

## A.1 client side changes
### A.1.1 ble_menu.c
In “amdtpMenuContent[AMDTP_MENU_MAX_ENTRIES][64]” add the information to display in the AMDTP menu.
### A.1.2 amdtp_svrcmds.h
Add to the structure “ eAmdtpPktcmd_t” the command to sent, As example we use AMD_CMD_XXX and add this after ‘AMDTP_AMDTP_CMD_PIN_LOW_PIN’

### A.1.3 amdtp_svrcmds.c

A.1.3.1 handleAMDTPSlection(void)
Add an entry for the menu selection as defined in A.1.1.

A.1.3.2 CmdInput()
In case additional information is required (like a pin ) add the call back in this routine. Look at the example as done for the others.

A.1.3.3 HandeServerResp(uint8_t * buf, uint16_t len)
Add an entry to handle the responds from the server on this command

## A.2 Server side changes
### A.2.1 amdtp.h

Add to the structure “ eAmdtpPktcmd_t” the command to sent, As example we use AMD_CMD_XXX and add this after ‘AMDTP_CMD_PIN_LOW’.
This place MUST be on the same place as done in step 1.1 for amdtcUI.h.

### A.2.2 amdtps.ino

A.2.2.1 UserRequestReceived()

Add to the ‘ switch (buf[0]) ‘ he option to capture the request. This can be anywhere in the test and the format is:
      case AMDTP_CMD_XXX:

        #if defined BLE_SHOW_DATA
        SERIAL_PORT.println("perform command XXX");
        #endif

        ACTION TO PERFORM ();
        break;

The format of the result to return is defined as follow :
val[0]	command requested by client ( AMDTP_CMD_XXX)
val[1] = *val_len = length of additional data
val[2] = *val_data = start of additional data

The additional data is free format, but make sure that Server and client know how to interpret these results. The val-buffer is defined for 100 bytes.
The correct values in *val_len and *val_data has to be set by the user. See other examples.
# Appendix B Check list for changes

CLIENT SOFTWARE CHANGES

- In amdtp_svrcmds.h add a new command to the eAmdtpPktcmd_t structure
- In ble_menu.c add display option to amdtpMenuContent
- In amdtp_svrcmds.c add in the handleAMDTPSlection() the option to the switch
- In amdtp_svrcmds.c add in the CmdInput() obtaining additional data (Optional)
- In amdtp_svrcmds.c add in the HandeServerResp() selection for server responds.

SERVER SOFTWARE CHANGES

- In amdtp.h add a new command to the structure
- In amdtps.ino add in the UserRequestReceived() a new test on command