Enabling deep sleep Apollo3

# 0. Background
I tried to understand how to save as much as possible power with an Apollo3 going in deep sleep. There are examples how to handle, but they are not complete and (after analyzing) not correct. See chapter 7.

# 1.0 What are advantages for Deep Sleep Mode
In Sleep Mode, the M4 is powered up, but the two clocks HCLK and FCLK are not active. The power supply is still applied to the M4 logic such that it can immediately become active on a wake-up event and begin executing instructions.

In Deep Sleep Mode, the main power of the M4 is removed, but the condition of the internal state is retained. The clocks are not active, and the MCU clock sources for HCLK and FCLK can be deactivated. To facilitate the removal of the source supply and entry into Deep Sleep Mode, the M4 will handshake with the Wake-up Interrupt Controller and Power Management Unit and set up the possible wake-up conditions. Greater than an order of magnitude less current draw can be achieved in Deep Sleep Mode compared to a similar configuration (SRAM, Flash, power domains) in Sleep Mode. (source: https://support.ambiq.com/hc/en-us/articles/360007459031-Q-A-What-is-the-difference-between-Sleep-Mode-and-Deep-Sleep-Mode-)

# 2.0 What can be set to deep sleep?
## 2.1 Flash memory
Flash memory, also known as flash storage, is a type of nonvolatile memory that erases data in units called blocks and rewrites data at the byte level. Flash memory is widely used for storage and data transfer in consumer devices, enterprise systems and industrial applications. Flash memory retains data for an extended period of time, regardless of whether a flash-equipped device is powered on or off. (source:https://www.techtarget.com/searchstorage/definition/flash-memory)

The Apollo3 Blue MCU Integrates up to 1024 KB of on-board Flash non-volatile memory and 16 KB of onetime programmable memory. These memories are managed by the APB flash controller for write operations.
During normal MCU code execution, the Flash Cache Controller translates requests from the CPU core (via the Flash cache) to the Flash Memory instance for instruction and data fetches. The controller is designed to return data in zero wait-states when accesses hit into the cache and can operate up to the maximum operating frequency of the CPU core. On cache misses, the controller issues miss requests to the Flash memory controller. (source: Apollo3 datasheet chapter 3.10.2)

In the Apollo3 processor there are 2 banks (Flash0 and Flash1) of 512K flash memory that can be put to sleep without loosing information.

The first 64KB (0x1000) is can not be used for storing code or (fixed) data. From 0x000 – 0xC00 is used by the Ambiq boot, 0xc00 – 0x1000 is reserved to store the Sparkfun variable loader (SVL). As such 1024KB – 64KB = 960KB flash memory available for sketches.
## 2.2 Cache memory
When the ARM architecture was first developed, the clock speed of the processor and the access speeds of memory were broadly similar. Processor cores today are much more complicated and can be clocked orders of magnitude faster. However, the frequency of external buses and of memory devices has not scaled to the same extent. It is possible to implement small blocks of on-chip SRAM that can operate at the same speeds as the core, but such RAM is very expensive in comparison to standard DRAM blocks, which can have thousands of times more capacity. In many ARM processor-based systems, access to external memory takes tens or even hundreds of core cycles. A cache is a small, fast block of memory that sits between the core and main memory. It holds copies of items in main memory. Accesses to the cache memory occur significantly faster than those to main memory. Whenever the core reads or writes a particular address, it first looks for it in the cache. If it finds the address in the cache, it uses the data in the cache, rather than performing an access to main memory. This significantly increases the potential performance of the system, by reducing the effect of slow external memory access times. It also reduces the power consumption of the system, by avoiding the need to drive external signals.(source : https://developer.arm.com/documentation#q=cache)

Apollo3 Blue MCU incorporates a Flash cache to the ICode (instruction) and DCode (data) path from the micro controller. This controller is intended to provide single cycle read access to Flash and reduce overall accesses to the Flash to reduce power. The controller is a unified ICode and DCode cache controller. The cache fill path is arbitrated between cache misses as well as the other Flash read agents (Info, Reg, BIST). Caching is supported for the entire 1 MB internal Flash and the 64 MB external Flash aperture (via MSPI). The cache is configurable 2-way set associative or direct mapped, 128b line size. (source: Apollo3 datasheet chapter 3.10.3)
## 2.3 SRAM
The Apollo3 has 384KB SRAM area which consists of 2 parts :

- Tightly-Coupled Memory or (TCM)
- Main SRAM area

TCM is the lower SRAM with a size of 64KB. The main SRAM area is 320KB in size and it broken down in 10 groups (group0 – group9) of 32KB SRAM that can individually be turned on and put to sleep depending on the size of volatile data that needs to be retained during sleep.

TCM and each SRAM group that is powered-down will loose all the information.
### 2.3.1 Tightly-Coupled Memory (TCM)
TCM is designed to provide low-latency memory that can be used by the processor. This memory can be used to hold critical routines, such as interrupt handling routines or real-time tasks where the indeterminacy of a cache would be highly undesirable. In addition, you can use TCM to hold ordinary variables, data types whose locality properties are not well suited to caching, and critical data structures such as interrupt stacks. A TCM is physically located very close to the processor core. Accesses to the TCM will typically be configured to capture or return data in a single cycle. The is DTCM for data and ITCM for instructions. By storing time-critical routines such as exception handlers in the TCM, the processor can have immediate access to the subroutine rather than having to wait for an initial code fetch from external memory. (source :https://developer.arm.com/documentation#q=tcm)

### 2.3.2 Main SRAM
The SRAM Interface translates requests from the CPU core and DMA controllers to the SRAM Memory Instances for instruction and data fetches. The SRAM interface is designed to return data in zero wait- states and can operate up to the maximum operating frequency of the CPU core. On Apollo3, the DTCM banks are guaranteed to be zero wait-state unless there is contention for that specific memory array with another requester (CPU I/D Bus or DMA Bus). The Main SRAM banks are zero wait-state for sequential accesses or 1-wait state for non-sequential accesses for I/D Bus accesses unless there is contention for that specific memory array with another requester (CPU I/D Bus or DMA Bus). DMA accesses to Main SRAM are always 0-wait state unless there is contention for that specific memory array. Prefetching is used on the I/D Bus accesses to Main SRAM to minimize/eliminate wait-state bubbles. Prefetching can be enabled/disabled for I and/or D Bus accesses.
The Interface contains arbitration logic for each SRAM instance which allows one of 2 bus slaves access (DMA or CPU) to the SRAM on any given cycle.
(source: Apollo3 datasheet chapter 3.10.4)

What part of the binary code is placed in TCM or main SRAM is determined by configuration files and the compiler.

## 2.4 Peripherals
Each peripheral, BLE, PDM, MSPI, IOM0, IOM1, IOM2, IOM3, IOM4, IOM5, MSPI, SCARD, ADC, UART0, UART1, can be individually put to deep sleep to save power. Depending on which peripheral is turned on, it seems to turn on a complete power domain (see chapter 4.2).

After deep sleep they will have lost the configuration information in the module itself, but also the GPIO setting will need to reinitialized.

# 3.0 Memory map
(Source : Apollo3 datasheet)

The flash memory is 0x0 – 0xFFFFF or 1024KB. This is made up by FLASH0 and FLASH1, each 512KB.

The TCM is on 0x10000000 – 0x10000FFF or 64Kb. This is constructed of GROUP0 and GROUP1 (each 32KB).

The SRAM 0x10010000 – 0x1005FFFF or 320Kb.

The boot loader ROM contains instructions that are executed upon power up of the processor. Once a valid reset vector is establish at offset zero in the flash memory, the boot loader transfers control to users application by issuing a POR type reset which causes the core to enter the reset vector in flash.(source: Apollo3 datasheet chapter 3.10.2)

# 4.0 Power control registers
(Source : Apollo3 datasheet chapter 3.6.3)

There is a sketch call ‘PowerCntrl’ with which you can display the different power control registers.
## 4.1 SUPPLYSRC / SUPPLYSTATUS
An Apollo3 can use of BLE/BUCK or SIMO Buck to get efficient power. This is not used on the Sparkfun boards. Interesting enough however that the buck is enabled, although LDO is used and no buck-hardware installed. It seems this was more used on the earlier A0-level Apollo3 chips

## 4.2 DEVPWREN / DEVPWRSTATUS
These registers are used to enable or disable peripherals. The following functions should be used

am_hal_pwrctrl_periph_enable(am_hal_pwrctrl_periph_e ePeripheral)
am_hal_pwrctrl_periph_disable(am_hal_pwrctrl_periph_e ePeripheral)

Valid values for ePeripheral are :

    AM_HAL_PWRCTRL_PERIPH_NONE,
    AM_HAL_PWRCTRL_PERIPH_IOS,	// HCPA (IO Slave)
    AM_HAL_PWRCTRL_PERIPH_IOM0,	// HCPB
    AM_HAL_PWRCTRL_PERIPH_IOM1,	// HCPB
    AM_HAL_PWRCTRL_PERIPH_IOM2,	// HCPB
    AM_HAL_PWRCTRL_PERIPH_IOM3,	// HCPC
    AM_HAL_PWRCTRL_PERIPH_IOM4,	// HCPC
    AM_HAL_PWRCTRL_PERIPH_IOM5,	// HCPC
    AM_HAL_PWRCTRL_PERIPH_UART0,	// HCPA
    AM_HAL_PWRCTRL_PERIPH_UART1,	// HCPA
    AM_HAL_PWRCTRL_PERIPH_ADC,	// ADC
    AM_HAL_PWRCTRL_PERIPH_SCARD,	// SCARD Controller (not used)
    AM_HAL_PWRCTRL_PERIPH_MSPI,	// Master SPI (for external flash)
    AM_HAL_PWRCTRL_PERIPH_PDM,	// PDM
    AM_HAL_PWRCTRL_PERIPH_BLEL,	// BLE controller
    AM_HAL_PWRCTRL_PERIPH_MAX	// all

To check whether a peripheral-power is enabled use the following function:

am_hal_pwrctrl_periph_enabled(am_hal_pwrctrl_periph_e ePeripheral, uint32_t *pui32Enabled)

It will NOT provide the exact information for all individual peripherals as the power is grouped in HCPA, HCPB, HCPC for IOS, IOM’s and UARTs. The grouping can be seen above. For ADC, PDM, BLE and MSPI you can find out the status for the individual peripheral.
If pui32Enabled is set to 1, the group / peripheral is enabled.

## 4.3 MEMPWREN
This register enables the individual memory groups. When set, power will be enabled to the groups also automatically after deep sleep.
If a memory group was power-up, you can power it down. E.g. if power to 384K SRAM was enabled, doing a call with AM_HAL_PWRCTRL_MEM_SRAM_192K, will power down all the SRAM ABOVE 192K. Remember the bottom 64KB is DTCM and as such 128KB of main SRAM is maintained. If a memory region was not powered, you can power it up with this call. E.g. if power to 192K SRAM was enabled, doing a call with AM_HAL_PWRCTRL_MEM_SRAM_224K, will power up to 224K SRAM.

This register works in connection with the MEMPWDINSLEEP register. Based on the setting in the MEMPWREN register, the MEMPWRINSLEEP register will determine whether (full) power is to be enabled to the memory after deep sleep. If the memory group in MEMPWREN register is not set, then power will stay disabled to the memory group after deep sleep.

To select the memory group(s) to power-up now (if not already) and to be powered up AFTER the next deep sleep use the following function:

am_hal_pwrctrl_memory_enable(am_hal_pwrctrl_mem_e eMemConfig)
Valid eMemConfig are :

    AM_HAL_PWRCTRL_MEM_NONE,	// only valid for SRAM + TCM
    AM_HAL_PWRCTRL_MEM_SRAM_8K_DTCM,	// Group0TCM0 (0KB-8KB)
    AM_HAL_PWRCTRL_MEM_SRAM_32K_DTCM,	// Group0TCM1 (8KB-32KB)
    AM_HAL_PWRCTRL_MEM_SRAM_64K_DTCM,	// Group0 + Group1
    AM_HAL_PWRCTRL_MEM_SRAM_96K,
    AM_HAL_PWRCTRL_MEM_SRAM_128K,
    AM_HAL_PWRCTRL_MEM_SRAM_160K,
    AM_HAL_PWRCTRL_MEM_SRAM_192K,
    AM_HAL_PWRCTRL_MEM_SRAM_224K,
    AM_HAL_PWRCTRL_MEM_SRAM_256K,
    AM_HAL_PWRCTRL_MEM_SRAM_288K,
    AM_HAL_PWRCTRL_MEM_SRAM_320K,
    AM_HAL_PWRCTRL_MEM_SRAM_352K,
    AM_HAL_PWRCTRL_MEM_SRAM_384K,
    AM_HAL_PWRCTRL_MEM_FLASH_512K,	// flash 0
    AM_HAL_PWRCTRL_MEM_FLASH_1M,	// flash 0 + flash1 (power off default)
    AM_HAL_PWRCTRL_MEM_CACHE,	// retain in deep sleep by default
    AM_HAL_PWRCTRL_MEM_ALL,
    AM_HAL_PWRCTRL_MEM_MAX

Note1: The function in the Sparkfun Apollo3 library works commulative. So you can NOT enable all the SRAM to 192K, power-down 192-352K and then also power-up the 352K – 384K. It highest memory selection will enable all the memory that is lower as well and it will also power-down any memory group that was enabled above this selection.

Note2: Although valid eMemConfig-options, the function will prevent Group0TCM0 and FLASH0 to be power-down / disable to avoid inadvertently disabling any memory currently being depended on.
## 4.5 MEMPWDINSLEEP
This register controls the power down or retain of the different memories in deep sleep mode.

In case of TCM or Main SRAM memory, if this is set, then the power for that SRAM group will be gated when the core goes into deep sleep. Upon wake, the data within the SRAMs will be erased. If this is not set, retention voltage will be applied to the SRAM groups when the core goes into deep sleep. Upon wake, the data within the SRAMs are retained. Do not set this(and thus power-down) if the SRAM bank is used as the target for DMA transfer while CPU in deep sleep.

This register is also used to enable/disable power-down of Flash0, Flash1 and cache during deep sleep. The flash and cache can be set to power down during deep sleep without losing information. After deep sleep the memory locations enabled with in MEMPWREN will be powered up. As cache is powered up it will clear and start from scratch, resulting in some extra time due to misses in cache where data needs to be retrieved from flash.

To set the behavior during the next deep sleep for which memory locations to go power-down:
am_hal_pwrctrl_memory_deepsleep_powerdown(am_hal_pwrctrl_mem_e eMemConfig)

To prevent memory locations going in deep sleep and thus content being retained you use:
am_hal_pwrctrl_memory_deepsleep_retain(am_hal_pwrctrl_mem_e eMemConfig)

## 4.6 DEVPWREVENTEN
This register controls which feature trigger that will result in an event to the CPU. It includes all the power on status for the core domains (peripherals), as well as the Burst event. If any of the bits are set, then if the domain is turned on, it will result in an event to the ARM core.

The Sparkfun Apollo3 library has no function to control these events. By default NO events are enabled.

## 4.7 MEMPWREVENTEN
This register controls which power enable for the memories will result in an event to the CPU. It includes all the power on status for the memory domains. If any of the bits are set, then if the domain is turned on, it will result in an event to the ARM core.
The Sparkfun Apollo3 library has no function to control these events. By default NO events are enabled.
# 5.0 How to put to deep sleep?
We need to make distinction between memory and on-chip peripherals.
## 5.1 Memory deep sleep
### 5.1.1 Default
By default during deep sleep the DTCM, SRAM and Cache are retained. Flash0 and Flash1 are powered-down.
By default after deep sleep the power to all memory locations (DTCM, SRAM, Cache, Flash0 and Flash1) are enabled.
### 5.1.2 Flash deep sleep
Flash0, Flash1 and Cache can be set to go in deep sleep without the change of loosing data.

### 5.1.3 TCM /SRAM deep sleep
You need to make sure that you keep all the SRAM is retained in deep sleep that is used by your sketch. Now it is a bit difficult to find exactly how much that is. The information after compiling a sketch can be of help, but you may need to find-out by testing.

#### V1.x.x library
With V 1.x.x the linker and startup_gcc.c are defined as part of each variant. The stack size is fixed in the startup_gcc.c at 80K (20K * 4 bytes (32 bitwords)). It is located at the start (address 0x0) of SRAM, which is actually the DTCM space. In SRAM it is followed by the .data section, .bss section and .heap.

When you compile you get information like:

Memory region Used Size Region Size %age Used
        FLASH: 17088 B 960 KB 1.74%
        SRAM: 115740 B 384 KB 29.43%

Sketch uses 17036 bytes (1%) of program storage space. Maximum is 960000 bytes.
Global variables use 33820 bytes of dynamic memory.

.text : 17036 bytes This it the compiled program binary code.
.data : 17088 – 17036 = 52. This is initialized data in the code that will be copied to SRAM.
.stack : This is fixed at 80KB or 81920 bytes.
.bss : 115740 – 81920 – 52 = 33768 bytes. These variables are not initialized in the code set to 0.
.heap: Starts at 115740 and is used for the dynamic memory allocation e.g.malloc() etc.

In this example ~113K of SRAM is used. Depending on how much malloc() is happening, it looks nearly save to disable any memory higher than 192KB.

#### V2.x.x library
With V2.x.x in the file AMA3B1KK.ld defines that the STACK is counting down.
It defines the __StackTop = ORIGIN(RAM) + LENGTH(RAM)-8. It counts down from there. 384K = 0x6000 = 393216 bytes and thus StackTop is at 393208 = 0x5FFF8.
It also defines _StackLimit = __StackTop – MBED_BOOT_STACK_SIZE. The later is defined as 0x400 = 1024 bytes. I can not grow further down.

As the stack starts in the top of memory, you must always retain the top group. In the Sparkfun Apollo3 library you can not select individual memory groups. The selection is commulative and thus retain the full 384K.

p.s. A further memory analyse as with V1.x.x will fail as the stack is set at top of memory, thus always showing a nearly 100% usage of SRAM and you must retain all the SRAM anyway.
## 5.2 On-chip peripherals
### 5.2.1 V1.x.x library
It works well for many as .end() will cause the right reset and start condition for the next .begin()
SPI.end() & Wire.end() will cause the IOM to powered-down and Apollo3 driver de-initialize.
Serial.end() : will cause the UARTx to powered-down and Apollo3 driver de-initialize.
RTC is normally used to wake up at a certain alarm time.

Exceptions:
PDM does not have an end() and extra work needs to be done to de-initialize and power down PDM correctly.
SoftwareSerial has an end() function but does not stop the CTIMER 7. Extra work is necessary if needed.
PWM could have the same impact as it uses a timer.
ADC must be disabled calling power_adc_disable() from the sketch before going to deep sleep. It will be enabled automatically with next AnalogRead or AnalogWrite.

### 5.2.2 V2.x.x library
First the bad news, if you are using V2.x.x boards library, there is a LOT more work that needs to happen to enable a peripheral after deep sleep. Turning off and then power on peripheral will result peripheral starting in default state. Hence the peripheral needs to be re-initialized.

During create a peripheral constructor or during begin() an new reference to MBED driver will be made. The MBED code sits in between the sketch libraries and the Apollo3 HAL driver.

Performing an .end() in V2 will not perform a de-intialize of the driver and not perform a power-down. In V2.x.x, depending on which peripheral it just deletes the reference to the MBED driver or does nothing.

From a sketch a peripheral can be powered-down and powered-up manually. Then doing a begin() will try to initialize of that peripheral. This will fail as the Apollo3 HAL driver still thinks/knows this was already done before and not repeat!

SPI.end(), Wire.end(): it will just delete the MBED link. There is NO way to recover. An adjustment to the SPI and Wire libraries are necessary to overcome. For Wire there is a github issue
https://github.com/sparkfun/Arduino_Apollo3/issues/412

PDM does not have an end() and work needs to be done to de-initialize and power down PDM correctly.
PWM could have the same impact as it uses a timer.

ADC: you must call powerControlADC(false) yourself from the sketch before going to deep sleep. It will be automatically be started and re-initialized with the next analogRead().

Serialx.end(), is an empty function, does nothing, it does not delete the MBED-driver link. From sketch the UART0 / UART1 can be powered-down and powered-up manually. In Serialx.begin() it will then try to re-initialize the UART, but the GPIO’s have to be reset from the sketch.

## 5.3 Program impact
Sketches of libraries can have an impact on the ability to go and stay correctly in sleep. One program is ArduinoBLE. This starts a CTIMER in Apollo3 in order to streamline the workflow for the BLE driver. When performing a BLE.end() it will just terminate the bleloop-threat without stopping the timer first. Hence directly after going in deep sleep, that timer will trigger a wake-up.
https://github.com/sparkfun/Arduino_Apollo3/issues/415

# 6.0 Conclusion
Deep sleep and Sparkfun Apollo3 boards library V2.x.x does not work well together if you use more than Serial and ADC. With the V1.x.x you stand a much better change, but there are still issue to overcome and to test as there can still be a program impact.

# 7.0 Remarks about sketches
1. Memory enable

In a number of sketches related to deep sleep you will find in wakeup() :

// Power up SRAM, turn on entire Flash
am_hal_pwrctrl_memory_deepsleep_powerdown(AM_HAL_PWRCTRL_MEM_MAX);

This is incorrect:
1. This just sets for the NEXT deep sleep ALL memory locations to power-down
2. The power-up after deep sleep is defined with am_hal_pwrctrl_memory_enable(). By default ALL memory locations are enabled to power-up after deep sleep.

2. ADC power
In gotosleep() you will find a call to powerdown ADC which is correct to do :
  powerControlADC(false) (V2.x.x) or power_adc_disable() (V1.x.x)

In wakeup() you find a call to power up ADC
  // Enable ADC
  initializeADC(); (V2.x.x)	OR	ap3_adc_setup(); (V1.x.x)

This enable is incorrect as it will power-up ADC while we might not use this at all. When calling analogRead() it will check that it was powered done and re-initialize.