Apollo-3 BLE communication between Apollo3 boards

# 1. Foreword

As part of a project to better understand Bluetooth, I have worked connecting boards from Sparkfun based on Apollo3. The connection is using the lightweight, propriety AMD Transaction Protocol.

The Apollo3 board is acting as a server and all actions are initiated by a client running on another Apollo3 board. The client has also been tested to run on with IDE 1.8.12.

An example BLE_led was available, but only provides the functionality to put a led on and off. Not very helpful. This solution can do MUCH more to exchange data.

March 2020,

Paul van Haastrecht
paulvha@hotmail.com

# 2. Hardware

## 2.1 Server board

The server software has been tested on a Redboard Artemis ATP (DEV-15442) and a Sparkfun Edge Development board (DEV-15170). On the later, not all pins are available, actually NONE of the ADC pins is available. So it better to have the ATP run as server.

Optionally an BME280 can be connected on both leveraging the QWIIC interface, or use the SDA / SCL connectors on the ATP. The Adafruit BME280 has been tested successfully.

## 2.2 Client hardware

The client software has been tested on a Redboard Artemis ATP (DEV-15442) and a Sparkfun Edge Development board (DEV-15170).

# 3. Software installation

## 3.1 Server software
### 3.1.1 Apollo3 software

Make sure you have the latest Apollo3 Arduino library. At the time of testing that was 1.0.30. Follow the steps on https://learn.sparkfun.com/tutorials/artemis-development-with-arduino?_ga=2.21301179.126288810.1581865370-203897739.1571077629

Select the right board in the Arduino IDE.

### 3.1.2 Application software

Select the folder with the BLE_amdts.ino. This folder contains other files that are necessary for compiling.

Make the optional changes in the top of the BLE_amdts.ino as defined in chapter 4.1.2.

Now compile and load the software to the board. On the Edge board you will have to manually set it in bootloader :

press and hold reset
press and hold button 14
release reset, while holding button 14

Once it starts uploading you can release button 14. After upload it might be necessary to press reset to start the program.

## 3.2 Client software

### 3.2.1 Apollo3 software

Make sure you have the latest Arduino library. Follow the steps on https://learn.sparkfun.com/tutorials/artemis-development-with-arduino?_ga=2.21301179.126288810.1581865370-203897739.1571077629

Select the right board in the Arduino IDE.

### 3.2.2 Client Application software

Select the folder with the amdtpc.ino. This folder contains other files that are necessary for compiling.

Make the optional changes to the client software see chapter 4.2.2.

Now compile and load the software to the board. On the Edge board you will have to manually set it in bootloader :

press and hold reset
press and hold button 14
release reset, while holding button 14

Once it starts uploading you can release button 14. After upload it might be necessary to press reset to start the program.

# 4. Software overview

## 4.1 Server Software

The server solution has been build with the Arduino Apollo3 software as created by Sparkfun. This software (1.0.30) is based on the Ambiqsuite SDK for the Apollo3. The AMD Transfer Protocol (AMDTP) has been taken from the AmbiqSuite and for the base for the sketch the Sparkfun provided example8_BLE_LED.ino. The server support (optional) an BME280, for which the software has been taken from Sparkfun BME280 library.

This software has also been tested by applying with the EXACTLE stack ported from Ambiq SDK 2.3.2 (which supports hashing). The software will auto-detect this option and adjust

### 4.1.1 High level overview

The core components are the EXACTLE Bluetooth stack, also known as CORDIO stack, which is part of the board package. The AMD transfer protocol, which is included as part of the additional file in the BLE_amdts directory (same as the .ino). Once initialized the server will wait for a client to connect and receiving data. With any data received it will call UserRequestReceived() in the sketch to handle the request on user level. Once completed the user will call SendReplyClient() with the data to return.

The format of the data is:
val[0] = requested command sent by Client, now returned to client
val[1] = length of any optional additional data (else 0)
val[2] = start of optional additional data

The format of the additional data is free form, maximum 100 characters. (see 4.1.3) It is the responsibility of the user to make sure Server and Client know how to interpret the data depending on the requested command.

NOTE: if the execution of a command too long, the Bluetooth stack might get stuck. See example of ‘chat’ how to overcome that.

### 4.1.2 Parameter setting

A number of parameters can be changed in the top of the sketch BLE_amdts.ino

#define BLE_PERIPHERAL_NAME "Artemis AMDTP BLE"
This defines the name of the server as it will show on Bluetooth.

#define MAXREPLY 100
Defines the maximum buffer length of data that can be submitted

#define INCLUDE_BME280
This enables including the BME280 software in the server. Default it is commented out.

ONLY VALID IF BME280 is selected
bool ALTM = true; sent Altitude in meters (true) or feet (false)
  bool TEMPC = true; sent temperature in Celsius (true) or Fahrenheit (false)

For DEBUG the following options are available, which are disabled by default. These need to be set in the additional file ble_debug.h:

#define BLE_Debug will show all the data and program flow
#define BLE_SHOW_DATA will only show the data received and sent
## 4.2 Client Software

The client solution has been build with the Arduino Apollo3 software as created by Sparkfun. This software (1.0.30) is based on the AmbiqSuite SDK for the Apollo3. The AMD Transfer Protocol (AMDTP) has been taken from the AmbiqSuite and for the base for the sketch the Ambiq Freetos amdtpc software was taken.

This software has also been tested by applying with the EXACTLE stack ported from Ambuiq SDK 2.3.2 (which supports hashing). The software will auto-detect this option and adjust

### 4.2.1 High level overview

The core components are the EXACTLE Bluetooth stack, also known as CORDIO stack, which is part of the board package. The AMD transfer protocol, which is included as part of the additional file in the amdtpc directory (same as the .ino).

Once initialized the client will show a 3 option menu: GAP, GATT and AMDTP. The first action is to scan for devices in the GAP menu (option 1), Once devices has been found, select Create connect90n (option 4) and select the devices index-number connect. Once connected, return to the main menu (option h) and select the AMDTP menu to interact with the server UI commands.

### 4.2.2 Parameter setting

The parameters are combined in the file ‘ble_menu.h’

//#define AM_DEBUG_PRINTF
This enables extended debug messages across all the files of the client solution. IN the top of each file this is translated to enable debug messages for that specific file. That might be handy if you focus on debugging only part of the file. (commented out by default)

#define BLE_MENU
Will enable the menu approach, in case later files should be used for other reasons.

#define AM_MENU_BUFSIZE 256
The buffer to display menu strings with am_menu_printf().

#define RXDATALEN 50
Maximum data length from keyboard input

# 5. Client Menu selection
## 5.1 Main menu
--------------BLE main menu--------------------
1. BLE_MENU_ID_GAP
2. BLE_MENU_ID_GATT
3. BLE_MENU_ID_AMDTP
hint: use 'h' to do main menu
 -----------------------------------------------------
The main menu has 3 options.

## 5.2 GAP menu

----------------------GAP menu----------------------
1. Start Scan
2. Stop Scan
3. Show Scan Results
4. Create Connection
5. Close connection
6. Toggle Through-put measurement

hint: use 'h' to do main menu
-----------------------------------------------------

1. Start scan :
will start the scanning process for other Bluetooth devices. Will time out after 4 seconds

2. Stop scan :
Manually stop scanning.

3. Show Scan result :
Will show an overview of the detected devices during scan.

--------------------Scan Results--------------------
0 : 0 66:77:88:23:BB:EF Artemis AMDTP BLE
----------------------------------------------------- ----
The
‘0 :’ is the index number
‘0’ is the address type defined as :

HCI_ADDR_TYPE_PUBLIC 0 /*!< \brief Public device address */
HCI_ADDR_TYPE_RANDOM 1 /*!< \brief Random device address */
HCI_ADDR_TYPE_PUBLIC_IDENTITY 2 /*!< \brief Public identity address */
HCI_ADDR_TYPE_RANDOM_IDENTITY 3 /*!< \brief Random identity address */
HCI_ADDR_TYPE_ANONYMOUS 0xFF /*!< \brief Anonymous device address */

66:77:88:23:BB:EF : the Bluetooth address

Artemis AMDTP BLE : name provided by the detected Bluetooth devices (if correctly detected)

4 create connection:
Will show the detected devices as mentioned above and now select the index number of the device to connect of press ‘h’ to return to main menu.

5. Close device :
Will close a current connection.

6. Toggle through-put measurement :
This will provide on regular inter fall the amount of bytes that have been received.

## 5.3 GATT menu
At this stage the GATT menu does not have any options to select.

## 5.4 AMDTP menu
Once connected the main menu will be show again and now selected option 3.

----------------------AMDTP menu----------------------
1. Request Server to send test data
2. Request Server to stop sending test data
3. Sent ‘Hello’ to server
4. Request battery level percentage
5. Request battery level percentage with load resistor
6. Request internal temperature in Celsius
7. Request internal temperature in Fahrenheit
8. Turn server onboard led on
9. Turn server onboard led off
10. Request BME280 measurement
11. Request ADC pin level
12. Request chat session
13. Request digital pin level
14. Set digital pin High
15. Set digital pin Low

hint: use 'h' to do main menu
-----------------------------------------------------

1. Start receiving test data
Entering 1<enter> the server will sent “test #” every second or so. The # will increment with each received message.

2. Stop receiving test data
Entering a 2 will instruct the server to stop sending test data. The menu will reappear.

3. Send hello
Just a test to check the connection is working. The server will reply with an “Hello” responds. The menu will reappear.

4. Battery level in percentage
The Apollo3 processor has an internal ADC sensor for the battery level, no additional hardware needed. This option will display the percentage of measured value / 3.3V (which is the expected voltage). Too high or TOO low can cause issues. The menu will reappear.

5. Battery level in percentage with load resistor
The Apollo3 processor has an internal ADC sensor for the battery level AND an internal load resistor ( ~500 ohm), no additional hardware needed. This option will display the percentage of measured value / 3.3V (which is the expected voltage). By first setting the resistor and then measure the percentage you get an impression about the quality of the supply under load. After measurement the resistor is removed. Much lower value than measure without load resistor can indicate weak power supply. The menu will reappear.

6 & 7 Read internal temperature in Celsius /Fahrenheit
The Apollo3 processor has an internal temperature measurement, no additional hardware needed. This option will display in Celsius or Fahrenheit that internal temperature and the menu will reappear.

8. Turn LED on
will turn ON the on-board led on the server. The menu will reappear.

9. Turn LED off
will turn OFF the on-board led on the server. The menu will reappear.

10. Read BME280 (if connected)
Optionally a BME280 can be connected to the server. This must be enabled in the sketch, see chapter 4.1.3 as well info in top of sketch. If enabled this will show the BME280 result. The menu will reappear.

11. Read ADC channel
After selecting this option you need to provide a valid ADC channel of the Apollo3 to be read. The results will be between 0 and 1023 and in volt. The menu will reappear.

12. Perform simple chat
This will allow to sent a line of text (max 45 characters) taken from the keyboard from the client to the server. It will wait for the server to respond, but not endless. The message will be displayed on the server and what is typed on the server is displayed at the client. If the server or the client is sending BYE, the connection will close and the menu will re-appear.

13. Read a digital pin
After selecting this option you need to provide a valid digital pin of the Apollo3 to be read. The result will be HIGH or LOW. The menu will reappear.

14 & 15 Set a pin HIGH or LOW
After selecting this option you need to provide a valid digital pin of the Apollo3 to be set. The menu will reappear.

# Appendix A : Adding an option

This describes the different steps to take to add an option between client and server

## A.1 client side changes
### A.1.1 ble_menu.c
In “amdtpMenuContent[AMDTP_MENU_MAX_ENTRIES][64]” add the information to display in the AMDTP menu.
### A.1.2 amdtp_svrcmds.h
Add to the structure “ eAmdtpPktcmd_t” the command to sent, As example we use AMD_CMD_XXX and add this after ‘AMDTP_AMDTP_CMD_PIN_LOW_PIN’

### A.1.3 amdtp_svrcmds.c

A.1.3.1 handleAMDTPSlection(void)
Add an entry for the menu selection as defined in A.1.1.

A.1.3.2 CmdInput()
In case additional information is required (like a pin ) add the call back in this routine. Look at the example as done for the others.

A.1.3.3 HandeServerResp(uint8_t * buf, uint16_t len)
Add an entry to handle the responds from the server on this command

## A.2 Server side changes

### A.2.1 BLE_amdtp.h

Add to the structure “ eAmdtpPktcmd_t” the command to sent, As example we use AMD_CMD_XXX and add this after ‘AMDTP_CMD_PIN_LOW’.
This place MUST be on the same place as done in step 1.1 for amdtcUI.h.

### A.2.2 BLE_amdtps.ino

A.2.2.1 UserRequestReceived()

Add to the ‘ switch (buf[0]) ‘ he option to capture the request. This can be anywhere in the test and the format is:
      case AMDTP_CMD_XXX:

        #if defined BLE_SHOW_DATA
        SERIAL_PORT.println("perform command XXX");
        #endif

        ACTION TO PERFORM ();
        break;

The format of the result to return is defined as follow :
val[0]	command requested by client ( AMDTP_CMD_XXX)
val[1] = *val_len = length of additional data
val[2] = *val_data = start of additional data

The additional data is free format, but make sure that Server and client know how to interpret these results.

The val-buffer is defined for 100 bytes.

The correct values in *val_len and *val_data has to be set by the user. See other examples.
# Appendix B Check list for changes

CLIENT SOFTWARE CHANGES

- In amdtp_svrcmds.h add a new command to the eAmdtpPktcmd_t structure
- In ble_menu.c add display option to amdtpMenuContent
- In amdtp_svrcmds.c add in the handleAMDTPSlection() the option to the switch
- In amdtp_svrcmds.c add in the CmdInput() obtaining additional data (Optional)
- In amdtp_svrcmds.c add in the HandeServerResp() selection for server responds.

SERVER SOFTWARE CHANGES

- In BLE_amdtp.h add a new command to the structure
- In BLE_amdtps.ino add in the UserRequestReceived() a new test on command