Apollo-3 BLE communication Apollo3 and Raspberry Pi

# 1. Foreword

As part of a project to better understand Bluetooth, I have worked connecting boards from Sparkfun based on Apollo3 over Bluetooth with Raspberry Pi. The connection is using the lightweight, propriety AMD Transaction Protocol.

The Apollo3 board is acting as a server and all actions are initiated by the Raspberry Pi, acting the client. The client has also been tested to run on Ubuntu 18.04.

An example BLE_led was available, but only provides the functionality to put a led on and off. Not very helpful. This solution can do MUCH more to exchange data.

February 2020,

Paul van Haastrecht
paulvha@hotmail.com

Version 1.1 / March2020
Minor Updates
# 2. Hardware

## 2.1 Server board

The server software has been tested on a Redboard Artemis ATP (DEV-15442) and a Sparkfun Edge Development board (DEV-15170). On the later, not all pins are available, actually NONE of the ADC pins is available.

Optionally an BME280 can be connected on both leveraging the QWIIC interface, or use the SDA / SCL connectors on the ATP. The Adafruit BME280 has been tested successfully.

## 2.2 Client hardware

Either use a Raspberry PI or a PC running Ubuntu. Starting Raspberry PI 3 is contains Bluetooth BLE on the board. For an Ubuntu PC you might need to obtain a separate Bluetooth dongle.

# 3. Software installation

## 3.1 Server software
### 3.1.1 Apollo3 software

Make sure you have the latest Arduino library. Follow the steps on https://learn.sparkfun.com/tutorials/artemis-development-with-arduino?_ga=2.21301179.126288810.1581865370-203897739.1571077629

Select the right board in the Arduino IDE.

### 3.1.2 Application software

Select the folder with the BLE_amdts.ino. This folder contains other files that are necessary for compiling.

Make the optional changes in the top of the BLE_amdts.ino as defined in chapter 4.1.2.

Now compile and load the software to the board. On the Edge board you will have to manually set it in bootloader :

press and hold reset
press and hold button 14
release reset, while holding button 14

Once it starts uploading you can release button 14. After upload it might be necessary to press reset to start the program.

## 3.2 Client software

### 3.2.1 Bluez Bluetooth stack

1. In the latest version of bluez (check on http://www.bluez.org/) :

wget https://www.kernel.org/pub/linux/bluetooth/bluez-5.52.tar.xz

2. Extract the source in a directory :

tar xvf bluez-5.52.tar.xz	(where 5.52 is the version)

3. Make sure you have the supporting packages :

sudo apt-get install libglib2.0-dev libdbus-1-dev libusb-dev libudev-dev libical-dev systemd libreadline-dev

4. enter the bluez-directory and type

.configure –enable-library

5. now build the bluez stack

make -j8 && sudo make install

Good support material for Bluez installation

https://www.jaredwolff.com/get-started-with-bluetooth-low-energy/#!

For Raspberry Pi there are extended instructions, but the one above should do
https://learn.adafruit.com/install-bluez-on-the-raspberry-pi/installation

### 3.2.2 Client Solution

cd bluez-5.52 (or what your version might be)

copy the 'amdtc'-directory as a complete directory + sub directory in this bluez directory

cd amdtc

(optional ?) update permissions : chmod +x make_amdtc

compile : ./make_amdtc

# 4. Software overview

## 4.1 Server Software

The server solution has been build with the Arduino Apollo3 software as created by Sparkfun. This software (1.0.29) is based on the Ambiqsuite SDK for the Apollo3. The AMD Transfer Protocol (AMDTP) has been taken from the AmbiqSuite and for the base for the sketch the Sparkfun provided example8_BLE_LED.ino. The server support (optional) an BME280, for which the software has been taken from Sparkfun BME280 library.

This software has also been tested by applying with the EXACTLE stack ported from Ambiq SDK 2.3.2 (which supports hashing). The software will auto-detect this option and adjust.

### 4.1.1 High level overview

The core components are the EXACTLE Bluetooth stack, also known as CORDIO stack, which is part of the board package. The AMD transfer protocol, which is included as part of the additional file in the BLE_amdts directory (same as the .ino). Once initialized the server will wait for a client to connect and receiving data. With any data received it will call UserRequestReceived() in the sketch to handle the request on user level. Once completed the user will call SendReplyClient() with the data to return.

The format of the data is:
val[0] = requested command sent by Client, now returned to client
val[1] = length of any optional additional data (else 0)
val[2] = start of optional additional data

The format of the additional data is free form, maximum 100 characters. (see 4.1.3) It is the responsibility of the user to make sure Server and Client know how to interpret the data depending on the requested command.

NOTE: if the execution of a command too long, the Bluetooth stack might get stuck. See example of ‘chat’ how to overcome that.

### 4.1.2 Parameter setting

A number of parameters can be changed in the top of the sketch BLE_amdts.ino

#define BLE_PERIPHERAL_NAME "Artemis AMDTP BLE"
This defines the name of the server as it will show on Bluetooth.

#define MAXREPLY 100
Defines the maximum buffer length of data that can be submitted.

#define ADC_RETRY 3
Due to an error in the current ADC core software the value is read a couple of times and then the average is returned. This defines how often to reading is done.

NOTE: The root cause is known and might be implemented in later core Arduino Apollo3 versions.

#define INCLUDE_BME280
This enables including the BME280 software in the server. Default it is commented out.

ONLY VALID IF BME280 is selected
bool ALTM = true; sent Altitude in meters (true) or feet (false)
  bool TEMPC = true; sent temperature in Celsius (true) or Fahrenheit (false)

For DEBUG the following options are available, which are disabled by default. These need to be set in the additional file ble_debug.h:

#define BLE_Debug will show all the data and program flow
#define BLE_SHOW_DATA will only show the data received and sent

## 4.2 Client Software
The Bluetooth stack is from Bluez (version 5.52) and the starting point is the solution is based on the source of gatttool, which is part of the package. The user interface is build from scratch.

### 4.2.1 High level overview

Most of the commands can be provided from the command line and if no specific action is requested, with the ‘-I’ option you can work interactive and provide the commands from a menu.
After connecting to the server, first ALL the primary UUID’s are extracted. Once connected the server will not advertise those anymore, so we store them in case we want to use them later. In this program we will only use the admtp service. Once we receive the requested handles of this service we will validate this against the known information and if match we assume we are connected to a known service.

We sent an “hello” message to the server and expect an answer. That way we known the server software is loaded with the right sketch. After that first the command line requests, if any, are executed. If interactive (-I) was (also) asked on the command line it is executed as the last option. Once all the commands are executed and, in case of interactive, the ‘quit’ option was selected the program will terminate. If the execution happened without an error the exit code will be EXIT_SUCCESS else EXIT_FAILURE.

### 4.2.2 command line options

Application Options:
  -i, --adapter=hciX	Specify local adapter interface
  -b, --device=MAC	Specify remote Bluetooth address
  -t, --addr-type=[public | random]	Set LE address type. Default: public
  -m, --mtu=MTU	Specify the MTU size
  -p, --psm=PSM	Specify the PSM for GATT/ATT over BR/EDR
  -l, --sec-level=[low | medium | high]	Set security level. Default: low
  -I, --interactive	Use interactive mode
  -q, --quiet ONLY display result
  -v, --verbose	Set verbose 0 = off, 1 = data only, 2 = all

The ONLY mandatory command is the ‘-b’ to provide the Bluetooth address of the server.

In interactive mode a menu is displayed as chapter 5.2.

Quiet will result in only the result numbers will be displayed, no sentence, just the value.
Can NOT be combined with verbose.

Verbose can be used to diagnose issues. By default it is ZERO and thus not providing any debug information. If set to ONE (1) it will show data received and sent only, while setting to TWO (2) it will also show the routines that are called and additional info.

commands
  --tempC	Read temperature in Celsius
  --tempF	Read temperature in Fahrenheit
  --battery	Read Battery percentage
  --battery with load	Read Battery percentage with load resistor
  --turnOn	Turn LED on
  --turnOff	Turn LED off
  --bme280	read BME280
  -A, --adc	read adc channel
  -R, --read	read digital pin
  -H, --high	set digital pin high
  -L, --low	set digital pin low

These are the command that can be exchanged with the server from the command line. Multiple commands can be included, where the command in A, R, H, L will need to have the ADC or digital pin added ( e.g. -A 29 will read ADC pin 29).

These commands can be used together with the interactive (-I) option. In that case first the command line commands will be executed before showing the interactive menu.
For explanation of the commands see chapter 5.2

By starting the application with the ‘--help-all’ option all the options are displayed.

# 5. Client usage
## 5.1. Obtaining the right Bluetooth address
Each Bluetooth device has a unique Bluetooth address. To obtain that Bluetooth address there are several options

On the smartphone (must support BLE Bluetooth) install the ‘nRF Connect’ app and select scanner. Look for: Artemis AMDTP BLE (unless you changed the name, see chapter 4.1.3)

On the Raspberry Pi / Ubuntu use the command that is part of the Bluez stack : sudo hcitool lescan

Output looks like :

LE Scan ...
65:39:02:5A:3E:23 (unknown)
66:77:88:23:BB:EF (unknown)
66:77:88:23:BB:EF Artemis AMDTP BLE

While you are in the amdtc directory :

To run the application interactive :	./amdtc -b 66:77:88:23:BB:EF -I
To read the ADC channel 29:	./amdtc -b 66:77:88:23:BB:EF -A 29
To first read ADC and then show interactive : ./amdtc -b 66:77:88:23:BB:EF -A 29 -I

You can add as many options as you like…
## 5.2 Interactive menu
When selecting interactive (-I) on the command line the following menu is displayed:

Make your selection :
0	Quit
1	Start receiving test data
2	Stop receiving test data
3	Read internal temperature in Celsius
4	Read internal temperature in Fahrenheit
5	Battery level in percentage
6	Battery level in percentage with load resistor
7	Turn LED on
8	Turn LED off
9	Read BME280 (if connected)
10	Read ADC channel
11	Read a digital pin
12	Set a pin HIGH
13	Set a pin LOW
14	Perform simple chat

Provide your choice :
Quit
Entering a 0 <enter> will close the program

Start receiving test data
Entering 1<enter> the server will sent “test #” every second or so. The # will increment with each received message. Can NOT be selected as command line option !

Stop receiving test data
Entering a 2 (NO ENTER) will instruct the server to stop sending test data. The menu will reappear.

Read internal temperature in Celsius / Fahrenheit
The Apollo3 processor has an internal temperature measurement, no additional hardware needed. This option will display in Celsius or Fahrenheit that internal temperature and the menu will reappear.

Battery level in percentage
The Apollo3 processor has an internal ADC sensor for the battery level, no additional hardware needed. This option will display the percentage of measured value / 3.3V (which is the expected voltage). Too high or TOO low can cause issues. The menu will reappear.

Battery level in percentage with load resistor
The Apollo3 processor has an internal ADC sensor for the battery level AND an internal load resistor ( ~500 ohm), no additional hardware needed. This option will display the percentage of measured value / 3.3V (which is the expected voltage). By first setting the resistor and then measure the percentage you get an impression about the quality of the supply under load. After measurement the resistor is removed. Much lower value than measure without load resistor can indicate weak power supply. The menu will reappear.

Turn LED on
will turn ON the on-board led on the server. The menu will reappear.

Turn LED off
will turn OFF the on-board led on the server. The menu will reappear.

Read BME280 (if connected)
Optionally a BME280 can be connected to the server. This must be enabled in the sketch, see chapter 4.1.3 as well info in top of sketch. If enabled this will show the BME280 result. The menu will reappear.

Read ADC channel
After selecting this option you need to provide a valid ADC channel of the Apollo3 to be read. The results will be between 0 and 1023 and in volt. The menu will reappear.

Read a digital pin
After selecting this option you need to provide a valid digital pin of the Apollo3 to be read. The result will be HIGH or LOW. The menu will reappear.

Set a pin HIGH or LOW
After selecting this option you need to provide a valid digital pin of the Apollo3 to be set. The menu will reappear.
Perform simple chat
This will allow to sent a line of text (max 45 characters) taken from the keyboard from the client to the server. It will wait for the server to respond, but not endless. The message will be displayed on the server and what is typed on the server is displayed at the client. If the server or the client is sending BYE, the connection will close and the menu will re-appear. Can NOT be selected as command line option.

# Appendix A : Adding an option

This describes the different steps to take to add an option between client and server

## 1 client side changes
## 1.1 amdtcUI.h
Add to the structure “ eAmdtpPktcmd_t” the command to sent, As example we use AMD_CMD_XXX and add this after ‘AMDTP_AMDTP_CMD_PIN_LOW_PIN’

## 1.2 amdtcUI.c
### 1.2.1 Top of program
Add the boolean for the option next to the others, around line 73:
extern gboolean opt_xxx;

NOTE : You can define the variable without “extern” if it is only used in Interactive, it that case define as 1.3.1 but now in amdtcUI.c

### 1.2.2 MainLoop()
Add to the ‘switch (buf[0])’ the option to display the results received from the server. This can be anywhere in the test and the format is:

        case AMD_CMD_XXX:
if (g_debug >0) g_print("\nexecute command XXX\n");

        g_print("OPTIONAL DISPLAY RESULTS”);
        break;

NOTE1 : if the first print is the ONLY conformation, one should leave out the ‘if g_debug’ to better understand what is happening interactive

NOTE2:
After an option is selected in interactive, it might be necessary to add extra information. In case a command needs additional values to be sent, follow the structure and add to the place where it states: if (GetValue == AMDTP_CMD_ADC).

### 1.2.3 display_menu()
Add at the current end of display_menu the information to display before making a selection
g_print("%d\tPerform Command XXX\n",sel++);

### 1.2.4 read_interactive()
Add at the end a selection for the option with the format

        case YY: // perform command XXX
        opt_xxx = TRUE;
        break;

The number to check (YY) must be equal to the number that is displayed with display_menu().

### 1.2.5 DetermineValue()
Add to the if-statement a check on the opt_xxx is true, then set the GetValue with the format
    else if (opt_xxx) {
        if (get) opt_xx = FALSE;
        GetValue = AMDTP_CMD_XXX;
    }
## 1.3 amdtc.c
### 1.3.1 Top of program

Add the boolean for the option next to the others, around line 73.
gboolean opt_xxx = FALSE;

see NOTE at 1.2.1. !!!

### 1.3.2 command line option
It is optional, but if you want to add performing command XXX to the command line options, add to ‘static GOptionEntry cmd_options[]’ the option. The format is as:

    { "turnOff", 0, 0, G_OPTION_ARG_NONE, &opt_TurnOff,
        "Turn LED off", NULL },

In case you want to provide a value to the option, look format in the example :
     { "adc", 'A', 0, G_OPTION_ARG_INT, &opt_adc_ch,
        "read adc channel", NULL },

This will allow to add on the command line ‘- -adc #’ or ‘-A #’. The value will be saved in ‘opt_adc_ch’, which was defined in in the top as ‘int opt_adc_ch = 0;’ and repeated in the top of amdtcUI.c as : extern int opt_adc_ch;
Also note the special check in main(), around line 666, to validate and enable the boolean.
## 2. Server side changes

### 2.1 BLE_amdtp.h

Add to the structure “ eAmdtpPktcmd_t” the command to sent, As example we use AMD_CMD_XXX and add this after ‘AMDTP_CMD_PIN_LOW’.
This place MUST be on the same place as done in step 1.1 for amdtcUI.h.

### 2.2 BLE_amdtps.ino

2.2.3 UserRequestReceived()

Add to the ‘ switch (buf[0]) ‘ he option to capture the request. This can be anywhere in the test and the format is:
      case AMDTP_CMD_XXX:

        #if defined BLE_SHOW_DATA
        SERIAL_PORT.println("perform command XXX");
        #endif

        ACTION TO PERFORM ();
        break;

The format of the result to return is defined as follow :
val[0]	command requested by client ( AMDTP_CMD_XXX)
val[1] = *val_len = length of additional data
val[2] = *val_data = start of additional data

The additional data is free format, but make sure that Server and client know how to interpret these results.

The val-buffer is defined for 100 bytes.

The correct values in *val_len and *val_data has to be set by the user. See other examples.
# Appendix B Check list for changes

CLIENT SOFTWARE CHANGES

- In amdtcUI.h add a new command to the structure
- In amdtcUI.c add in the top the external variables
- In amdtcUI.c add in the MainLoop() the option to the switch
- In amdtcUI.c add in the MainLoop() obtaining additional data (Optional)
- In amdtcUI.c add in the display_menu() a line to display the new selection
- In amdtcUI.c add in the read_interactive() a test on the new selection
- In amdtcUI.c add in the DetermineValue () a test on the new selection
- In amdtc.c add in the top the new variables
- In amdtc.c add in the command line option for the new selection (optional)

SERVER SOFTWARE CHANGES

- In BLE_amdtp.h add a new command to the structure
- In BLE_amdtps.ino add in the UserRequestReceived() a new test on command