# Overview of data transfer with ArduinoBLE

# Background
ArduinoBLE is a good library. Easy to use, it has good documentation and good examples. Especially if use small data packages, up to the maximum characteristic value-size of the MTU-size it is very straightforward. However for larger data packages it is challenging. This document tries to help out.

# What is MTU ?

MTU stands for Maximum Transmission Unit .

It is important to understand this aspect as part of larger datapackages.

In Bluetooth the data is transferred in packets. Next to the data within in each packet, there are additional control bytes (or octets). They help to get the data to the right place.

The picture above is taken from https://punchthrough.com/maximizing-ble-throughput-part-2-use-larger-att-mtu-2/ If you want to, quickly, better understand take a look there.

The MTU is what is called ‘ATT Data’ in the picture above. As you can see below there are 3 more control bytes. As such the real size to store data is MTU – 3.

The default MTU size is 23 bytes (octets), this is the minimum by standard. Which leaves 20 bytes (octets) for data.
Many modern processor chips support BLE with integrated HCI-layer. The layers above (L2CAP, ATT, GAP, GATT etc) are handled by software / drivers. Although the default MTU size is 23, it could be increased. Especially when you do transfer of large amount of data this can be interesting.

In ArduinoBLE the maximum MTU size a peripheral/central can handle is determined during BLE.begin(). From here in the HCI-layer readLeBufferSize() is called. This function obtains the maximum packet length and maximum # packets that can be queued in the HCI chiplayer. From that packetlength it then subtracts 9 bytes for the ACL head to the HCI :

  uint8_t pktType;	COMMAND_PKT, ACLDATA_PKT, EVENT_PKT, SECURITY_PKT
  uint16_t handle;	connection handle
  uint16_t dlen;	plen + 4 (handle + plen)
  uint16_t plen;	length of octets in MTU (include ATT header)
  uint16_t cid;	channel ID ( e.g. 4 = attribute, 1 = L2CAP signal)

This is used for internal routing and for the HCI layer to create the right BLE package. What is left is the maximum MTU size, but we still use the default 23 bytes.

An MTU size increase can be agreed between peripheral and central after connect. ONLY the central / client should perform that request.

In ArduinoBLE the call discoverAttributes() will perform that following functions :
      Request to remote to increase to it's max. MTU size
      Discover Services (with of without UUID filter)
      Discover characteristics (with of without UUID filter)
      Discover Descriptors (with of without UUID filter)

A client / central has a maximum MTU, but so has the peripheral / server. They do not have to be the same. As part of the protocol to agree on a different MTU-size, the client / central requests an MTU-size up to it's maximum MTU. The peripheral / server will respond with agreement or lower size that is depending on it's maximum MTU. Once that has finished both have the new agreed MTU which will be used. It could have been increased, but maybe it is still 23.

BUT what has been agreed ???

In many implementations of the BLE stack there is no standard function to obtain the agreed MTU, same with ArduinoBLE. Hence ArduinoBLE_P (P = Patched) has been enhanced to provide that information. The call readMTU() will provide the agreed MTU-size MINUS the 3 ATT bytes(octects). So you then know the size for data that will fit in the agreed MTU.

## MTU-size versus Characteristic value-size

In ArduinoBLE it is an important to understand the relationship MTU-size and maximum characteristic value-size.

With the integrated HCI layer in the Apollo3 / Artemis the maximum MTU size is 242 ( maximum packetlength - 9). The maximum data-portion of the MTU is 239 ( 242 - 3 ATT overhead). With ArduinoBLE_P you can use readMTU() to get this size.

However you can specify a maximum characteristic valuesize of 512 ?

What now ?

In the standard ArduinoBLE V1.2.3 version, the peripheral will send the data up to the agreed MTU-size. It is now down to the central to ask for the next ‘blob’ until it has read all the bytes. However if your central /client is also build with ArduinoBLE, it will not do that. The rest is neglected, not asked from the central, not send, disgarded, neglected !

OHOH !

BUT… you are lucky to have the ArduinoBLE_P (P = patched). In the ATT layer it tries to include as much as possible bytes to send in the each MTU-size. The central / client will read / receive the packet. If that is less than the expected amount of bytes in the central it will ask for next ‘blob’ starting with an offset from previous received bytes.

However, no matter what, if your characteristic uses notify to send the data. Whatever fits in the MTU-size will be send. The rest is neglected. Sorry, but you can only send ONE notification size !!

So what about speed ?

Using example12 on ArduinoBLE_P you can see below the impact of different blocksizes:

  blocksize
  100 : it takes about 2900 mS to sent a data packet of 874 bytes.
  200 : it takes about 1450 mS to sent a data packet of 874 bytes.
  300 : it takes about 870 mS to sent a data packet of 874 bytes.(only ArduinoBLE_P !)
  400 : it takes about 848 mS to sent a data packet of 874 bytes.(only ArduinoBLE_P !)
  500 : it takes about 507 mS to sent a data packet of 874 bytes.(only ArduinoBLE_P !)

Above 200 (actually 239) the packet does not fit in a single agreed MTU-sizde. AruindoBLE_P has been adjusted to take care of that !!
# Approach
A large message is broken down in smaller blocks of a size that fits within the defined characteristic value-size. All the blocks have a block-sequence number, indication of its length and has a 16 bit CRC to guarantee the integrity. The first block of a message has additional information about the size of the total message to transfer. Also the first block has a magicnumber so we know for sure central and peripheral are in sync. To guide the correct sequence there is small protocol.
Any request or error exchanged between central and peripheral is acknowledge with RECEIVED_OK.

# Sequence
The central is requesting for a new message (REQ_MESSAGE). The peripheral will respond with RECEIVED_OK.

The peripheral will then create the first block of the message and writes that to the characteristic. It will then send a NEW_BLOCK_AVAILABLE to the central with notify characteristic.

The central will read the block.

The first byte in the first block of a new message must be the MAGICNUM, if not an MAGIC_INVALID will be send. See ‘Error Handling’ later on. The central will now extract the length of total message from the header. Any previous obtained message memory is released. The new message may have a different size and it tries to obtain this memory. If that fails it will send ERR_INTERNAL message.

For any block (including the first) it will check for the correct block_sequence_number. If not an BLOCK_INVALID will be send. Also a check that the data portion + 2 bytes are the same a the read block length, else also BLOCK_INVALID.
Now the block data-portion is copied / added in the total message buffer. Once that has been done a CRC check is performed. If that does not match a CRC_INVALID will be send and copied /added data is removed from the message buffer. For next steps see ‘Error handling’.

If all is good a RECEIVED_OK is send to the peripheral. If the complete message length is not received yet, the central will send REQ_NEW_BLOCK. If all has been received, the central can handle the received message, e.g. display. The central sends RCD_CMPLT_MSG, to make sure that peripheral and central are in sync. The peripheral will respond with RECEIVED_OK and the transfer protocol is now complete.

After the peripheral receives REQ_NEW_BLOCK will respond with RECEIVED_OK.
The peripheral will create the next block of the message and writes that to the characteristic. It will then send a NEW_BLOCK_AVAILABLE to the central with notify. This will continue as described above until the complete message has been transferred, or a CANCEL_MESSAGE is received. In that case the transfer is canceled.

The peripheral also has the option to send a CANCEL_MESSAGE. This is a menu option. In that case the central will ignore any data that was transferred before.

### Example14 with MTU.

When using MTU-size instead of a fixed block next to the above it will perform extra activity

In case of example14, using the agreed MTU size instead of a fixed Block Length, the central will send a REQ_BLOCKSIZE to the peripheral after connect. The peripheral will send a RSP_BLOCKSIZE with the agreed MTU size. This MTU size has already the 3 byte ATT subtracted.

The agreed MTU size will also be included in the header of the first block. The central will check that this matches the earlier provided MTU size. Maybe the exchange MTU had not happened before. If no match the central it will send BLOCK_INVALID.

# Message format - example12
When a fixed block size is used :

  Block 0
  Byte 0 = MagicNum
  Byte 1 = MSB total message length (uint16_t)
  Byte 2 = LSB total message length
  Byte 3 = block number (starting 0) (uint8_t)
  Byte 4 = MSB block data length (excluding 2 bytes CRC) (uint16_t)
  Byte 5 = LSB block data length
  byte 5 - N data (N is MAX MAXBLOCKSIZE -3)
  Byte N +1 = MSB CRC on ALL previous bytes in block (uint16_t)
  Byte N +2 = LSB CRC

  blocks following
  Byte 1 = current block number X (uint8_t)
  Byte 2 = MSB block data length (excluding 2 bytes CRC) (uint16_t)
  Byte 3 = LSB block data length
  Byte 4 - N data (N is MAX MAXBLOCKSIZE -3)
  byte N +1 = MSB CRC on ALL previous bytes in block (uint16_t)
  Byte N +2 = LSB CRC

## Message format : example14

The block size is depending on the agreed MTU size

  Block 0
  Byte 0 = MagicNum
  Byte 1 = MSB total message length (uint16_t)
  Byte 2 = LSB total message length
  Byte 3 = Max block size depending on agreed MTU
  Byte 4 = current block number X (uint8_t)
  Byte 5 = block data length (excluding 2 bytes CRC) (uint8_t)
  Byte 6 - N data portion (N is MAX MTU size - 2)
  Byte N +1 = MSB CRC on ALL previous bytes in block (uint16_t)
  Byte N +2 = LSB CRC

  Blocks following:
  Byte 1 = current block number X (uint8_t)
  Byte 2 = block data length (excluding 2 bytes CRC) (uint8_t)
  Byte 3 - N data portion (N is MAX MTU size - 2)
  Byte N +1 = MSB CRC on ALL previous bytes in block (uint16_t)
  Byte N +2 = LSB CRC

## Protocol sequence example

  peripheral	central
  =============================================
  Advertise
Connect
read attributes

…………………………………………………………………...…….
 REQ_BLOCKSIZE	(example 14 only)
 Send Received_OK
 RSP_BLOCKSIZE
Send Received_OK
………………………………….………………………………..
  Wait for request
        send request for message (REQ_MESSAGE)
  Send Received_OK
        Wait for notification
  prepare block
  add CRC
  write block
  write notification
        Read / receive block
        check for correct block etc
        if not correct, request resend block#
  resend block
        else extract & store relevant data
        write peripheral all RECEIVED_OK
        if NOT complete request next block
  Send Received_OK
        Wait for notification
  prepare block
  add CRC
  write block
  write notification

# Error handling
Both central and peripheral can send an error.
All errors will be acknowledged by the receiver with RECEIVED_OK.
## Central
In case of the central the following errors can be send :

1. MAGIC_INVALID
The first byte in the first block of a new message is NOT the MAGICNUM.

2. INVALID_ BLOCK
In case the block_sequence number is out of sync OR the total length of the received block does not equal the data_length + 2 CRC bytes

3. CRC_BLOCK
The CRC check failed on the data portion of the block.

4. REQ_INVALID
An out of sequence command was received. The command will be ignored.

5. ERR_INTERNAL
This could the case when we can not read the block, can not allocate the right memory or block length do not match between peripheral and central

6. TIMEOUT_BLOCK:
If the time between the blocks receiving takes to long. (not yet implemented)

Upon receiving RECEIVED_OK from the peripheral in case of an sent error MAGIC_INVALID, INVALID_ BLOCK, CRC_BLOCK, ERR_INTERNAL the central will request a resend of the block. It will continue to do so for maximum RETRYCOUNT. If that is reached a CANCEL_MESSAGE will be send.

## Peripheral

In case of the peripheral the following errors can be send :

1. REQ_INVALID
An out of sequence command was received. The received command will be ignored.

# Routine overview
## Peripheral

void ReadCallBack(BLEDevice central, BLECharacteristic c);
Called when the central is reading. No action, information only.

void WriteCallBack(BLEDevice central, BLECharacteristic c) ;
called when a command has been written by the central. so we read.

void HandleCentralReq();
Act on received command/errors from central

void CreateSendBlock();
Instruct and check to send new block

uint8_t CreateDataToSend();
Breakdown message in block to be send.

void SendBlock();
Send block on characteristic and let central know on Notify

void SendCommand(uint8_t cmd);
Send a command on notify

void HandlePendingCmd();
Called when central has sent a RECEIVED_OK

void handle_input(char c);
Handle keyboard input

void display_menu();
Display the keyboard input menu options

void blePeripheralConnectHandler(BLEDevice central);
call-back on connect

void blePeripheralDisconnectHandler(BLEDevice central)
call-back on disconnect

## Central

void GetGoing();
(re) start BLE advertising and obtain Mtu (example12)

void HandlePeripheralCmd();
take action on command received from peripheral

void RetryBlock();
Retry sending new block after error only for RETRYCOUNT times

void SendCommand(uint8_t cmd);
Send command to peripheral on write characteristic.

void ReadDataBlock();
Read, parse each received block to compile a total message

void HandlePeripheralNotify(const uint8_t buf, uint16_t len);
Act on received commands from peripheral on the notify characteristic

void handle_input(char c);
get and act on local keyboard input

void DisplayMessage() ;
Display complete received message

void WaitToReconnect();
Wait to reconnect after disconnect from peripheral