Ambiq Micro Data Transfer Profile (AMDTP)

Based on a document (AMDTP_example_user’s_guide) which was published in 2017 and some of the sample code that are part of the SDK, I have build a version that can run on the Sparkfun V2.x.x. library. The mentioned document is also added in the extras folder.

In this document I want to describe on high level the routines using the example MBED-BLE_example16_gattserv_AMDTP_BME280. I will not describe the BME280 calls, but focus on AMDTP.

Regards

Paul van Haastrecht

note1:

Peripheral and server indicate the same : the sketch that is providing the data. I will only use the name server in this document.

Central and client indicate the same : the sketch that is obtaining / reading the data. I will only use the name client in this document.

# Folder structure

In the main folder ‘MBED-BLE’ are the following files and directories

MBED-BLE – files :
AUTHORS : who wrote / contributed to this
keywords.txt	: contain different routines, variables and constants that can be used
library.properties : information about the library and versions
README.md : information to display on github page
SetDebugBLE.txt : how to enable different debug messages in MBED

MBED-BLE/src-folder:
amdtpc.h	: header file to include for central / client sketch
amdtps.h	: header file to include for peripheral / server sketch
ble_debug.h	: contains calls to display Mbed debug messages (auto included
mbed_ble.h	: includes to compile correctly (auto included)
pretty_printer.h : different routines to support display (auto included)

MBED-BLE/src/amdtp-folder:
amdtp_common.h : common definition for AMDTP
crc32.c / crc32.h : to calculation CRC

MBED-BLE/src/amdtp/amdtps-folder:
amdtpServ.h	: here the AMDTP service is defined
amdtps_protocol.cpp / amdtps_protocol.h	: handle the AMDTP for server
gatt_server_amdtp.cpp / gatt_server_amdtp.h : gatt server

MBED-BLE/src/amdtp/amdtpc-folder:
amdtpc_protocol.cpp /amdtpc_protocol.h	: handle the AMDTP for client
gatt_client_amdtp.h	: connect to client /central sketch
# AMDTP peripheral / server
## sketch
The sketch is working 3 ways : receive a command from the client, regular send BME280 data and act on a local enter command. The commands are the same between client and server, based on a similar menu selection. The command are defined as:
enum key_input{
 REQUEST_METERS = 1,
 REQUEST_FEET,
 REQUEST_CELSIUS,
 REQUEST_FRHEIT,
 REQUEST_STOP,
 REQUEST_START,
 REQUEST_NOW,
 REQUEST_SHOW
};

The Cordio event_queue handler is used and this is defined with

static events::EventQueue event_queue(/* event count */ 16 * EVENTS_EVENT_SIZE);

The connection the MBED BLE is made with a constructor :

BLE& ble_instance = ble_instance.Instance();

The connection the library (amdtpServ.h) is made with a constructor :

GattServAMDTP BmeSvc(ble_instance, event_queue);

In setup() the name of the device is with :

  BmeSvc.set_device_name(_device);

Every time there is an even it will be processed by the event handler. This is initialized in setup():

ble_instance.onEventsToProcess(schedule_ble_events);

Once the event_queue is started it will not return and thus normal setup(), loop() sketch loop structure is not working. Instead a routine ( Check_loop()) is called every so 450 ms.

static const std::chrono::milliseconds CHECK_RATE_MS = 450ms;
event_queue.call_every(CHECK_RATE_MS, &Check_loop);

To initialize the service and start the event_queue a final call is made :
BmeSvc.start();

Check_loop() will check for local keyboard input, if any command was received from the client and perform sending regular updates.

StoreDataReceived() is hard-coded called whenever new data from the client has been received. The best is to hand it off (copy) instead of handling the command directly. Handling is called from within Check_loop()
## gatt_server_amdtp.h
When creating the constructor it will store the different supplied values in the library and create a constructor the AMDTP. The sketch is not dealing with the AMDTP code directly, all is handling through GattServAMDTP.

Start()
Here the BLE stack of MBED will be set to initialize, _ble.init(), and once completed it will return to on_init_complete(). The AMDTPS protocol is initialize with _tp.amdtps_init() and a call back to the protocol is set back to Data_From_AMDTP when received data has been processed.
Now the event_queue is started (_event_queue.dispatch_forever();) and the BLE_init is handled.

on_init_complete()
Called when the MBED BLE-stack is initialized. If that is successful it will set this class as the pointer for each virtual event calls ( onxxxxx). The onDataWritten call back is set in case the notify handler is written. As a final step it will start advertising

onDataWritten()
Any data-packet that is received will be passed on the AMDTP protocol AmdtpReceivePkt()

Data_From_AMDTP()
This callback was set during Start() and any complete received / processed data-packet coming from the protocol handling is passed back to the sketch StoreDataReceived()

SendToCentral()
This routine will pass the request to sent data to the protocol handling with AmdtpSendData(). When the processed data-packet is less than the default MTU size ( 23 – 3 = 20 bytes) it can be send within on AMDTP packet and complete in one transaction. The maximum raw data packet is then 12 bytes ( 8 byte AMDTP overhead on packet). If it needs to send multiple packages a time-out is set to prevent a deadlock. Next to that the sketch can call IsSendingComplete() to detect whether the AMDTP transaction has been completed.

## amdtps_protocol

As the constructor is created (called from gatt_server_amdtp) it will create a constructor with the AMDTP service definition in amdtpServ.h

amdtps_init()
This is called from start in gatt_server_amdtp. It will set different pointers and buffers to the start position.

AmdtpReceivePkt()
This is called from onDataWritten in gatt_server_amdtp. When the first AMDTP packet is received it will contain a length field (16 bits) and header (16 bits). The length field is the sum of all the data that should arrive + 4 byte CRC. The packet can either be a real data packet for the sketch program or internal ACK or control package. These will be stored in different buffers.
As it receives the length and header data is stored. The rest of the received data is stored in the selected buffer. With the next AMDTP packet all the received data is added into the buffer, until the complete length has been received. The last 4 bytes in the receive buffer are the CRC-32 bytes. A CRC-32 calculation is performed over the buffer in the receive buffer (minus the last 4 bytes). If that calculated CRC matches the received CRC-bytes the packet has been received successful. An ACK will be send to the sender to indicate successful. completion. Now the received data is passed on to AmdtpPacketHandler()

******************************************************************************
NOTE 2: If the complete data has not been completed an extra step had to be added.
The sending from server/peripheral is happening on a notify characteristic. We can send very quickly on that, but the client/central side it needs to be able to keep up with that speed with enough buffers. That is often NOT the case if you send 26 packet ( 512 / 20) very fast and package are dropped on the receiving side.

Hence I have implemented that after each chunk / packet has been sent, the sending side (either client/central or server/peripheral) will wait for the other side to confirm it has received this packet. Only after that it will send the next chunk / packet. This is indicated in the header with setting the ACK-bit by the sender and only needed for sketch data-packages. Not for internal ACK or Control.

The result is that all the packets are received, BUT each packet will take a turn-around time of 375ms. Measured between Artemis Edge and Artemis ATP board. Thus sending 512 bytes will take 10s on an a default MTU size.

When connecting to BLEAK (on Ubuntu) the 512 bytes takes 3 seconds. MUCH faster, but still
3000 / 512 = 6ms per byte = 1000 / 6 = 160 bytes per second.

Not fast... but for many sensor this speed will be acceptable as most produce only a small amount of bytes.

*******************************************************************************

AmdtpPacketHandler()
Once the complete package has been received, recombined and checked it will pass it on. Here it will check whether the package is data for the sketch and if so it will call the stored call back function (Data_From_AMDTP ) as set in start in gatt_server_amdtp.
The package also be an ACK in reaction on previous sent data. The status is checked to see whether it was successful. or failed.

The package can also be a CONTROL package. One of the control request AMDTP_CONTROL_SEND_READY, meaning start sending the next AMDTP package. (see note 2)

AmdtpSendData()
Is called from SendToCentral() in gatt_server_amdtp. It will call AmdtpsSendPacket() with the type of packet to send.
In AmdtpsSendPacket() it will perform some checks and it will then call AmdtpBuildPkt() to create the AMDTP packet to be send. As a last point it will call AmdtpSendPacketHandler(0 to perform sending the packet in chunks

AmdtpBuildPkt()
Here the AMDTP package is build. It will add the length and the header. If the length (including overhead bytes) is longer than the MTUsize – 3 (most of the time 23 – 3 = 20 bytes), it will set the ACKbit in the header to indicate that after each packet an confirmation is required. It copies the data to send and the CRC-32 to the packet

AmdtpSendPacketHandler()
This routine can be called multiple times. The first time it will initialize and then send the first packet. If sending the complete package takes multiple chunk of MTU-size – 3 bytes, it will wait until is called again from AmdtpPacketHandler() as the control package was received from the other side indicating the previous chunk had arrived. If the complete package has been send, it will indicate that it is done and now waiting on an ACK from the receiver that the CRC-32 was correct.

AmdtpSendComplete()
This is called from IsSendingComplete() it will check with the flag is set or cleared that the complete package in chunks was send.

# AMDTP central / client
## sketch

The sketch is working 2 ways : Send a command to the server, regular send BME280 data . The commands are the same between client and server, based on a similar menu selection. The command are defined as:
enum key_input{
 REQUEST_METERS = 1,
 REQUEST_FEET,
 REQUEST_CELSIUS,
 REQUEST_FRHEIT,
 REQUEST_STOP,
 REQUEST_START,
 REQUEST_NOW,
 REQUEST_SHOW
};

The Cordio event_queue handler is used and this is defined with

static events::EventQueue event_queue(/* event count */ 16 * EVENTS_EVENT_SIZE);

The connection the MBED BLE is made with a constructor :

BLE& ble_instance = ble_instance.Instance();

The connection the library (amdtpServ.h) is made with a constructor :

GattClientProcess ble_process(event_queue, ble_instance);

In setup() the name of the device to look for :

  ble_process.set_peer_device_name(peer_device);

Once the event_queue is started it will not return and thus normal setup(), loop() sketch loop structure is not working. Instead a routine ( Check_loop()) is called every so 450 ms.

static const std::chrono::milliseconds CHECK_RATE_MS = 450ms;
event_queue.call_every(CHECK_RATE_MS, &Check_loop);

To initialize the service and start the event_queue a final call is made :
BmeSvc.start();

Check_loop() will check for ConnectionComplete(). This means the AMDTP discovery has been completed. It will display the command menu and check for any keyboard input.

StoreDataReceived() is hard-coded called whenever new data from the client has been received. The new data can be an echo of a command send earlier or BM280 data to display.

## gatt_client_process.h
This file is located with the sketch and will connect with the library it will perform the following functions about connecting with the remote server :

 Initialize the MBED BLE stack
 Set peripheral devicename to look for
 Call a function after ble.init or connection has completed
 Select a scanned device based on the device name
 Start connection to the selected device
 Restart scan after disconnect

Start()
Here the BLE stack of MBED will be set to initialize, _ble.init(), and once completed it will return to on_init_complete().

Every time there is an event it will be processed by the event handler. This is initialized in setup():

ble_instance.onEventsToProcess(schedule_ble_events);

A number of callback routines are initialized between the library gatt_client_amdtp.h and this file.
In gatt_client_amdtp.h the server is discovered. The connect are on_init, on_connect and on_disconnect

Here the BLE stack of MBED will be set to initialize, _ble.init(), and once completed it will return to on_init_complete().

Now the event_queue is started (_event_queue.dispatch_forever();) and the BLE_init is handled

SendToCentral()
This routine will pass the request to sent data to the library to be send. When the processed data-packet is less than the default MTU size ( 23 – 3 = 20 bytes) it can be send within on AMDTP packet and complete in one transaction. The maximum raw data packet is then max 12 bytes ( 8 byte overhead on first packet). If it needs to send multiple packages a time is set to prevent a deadlock. Next to that the sketch can call IsSendingComplete() to detect whether the AMDTP transaction has been completed. In the case of BME280 however it is only one byte.

IsSendingComplete()
Can be called to check that sending has been completed in case off multi chunks needed to be sent.

Data_From_AMDTP()
is called by the protocol with a proposed complete data package for the sketch. It is passed to the sketch with a hard-coded StoreDataReceived()

when_characteristic_changed()
Any data received by the client triggers this routine. The received data is passed on the the AMDTP protocol AmdtpReceivePkt()
## gatt_client_amdtp.h
When creating the constructor it will store the different supplied values in the library and create a constructor the AMDTP. The sketch is not dealing with the AMDTP code directly, all is handling by of through GattClientAMDTP.

Start()
The different provided variables are stored and a filter is set on the AMDTP service as well as the characteristics. The connection with the AMDTP protocol is set in case an ACK, data need to be send, or when a complete data package has been received to be forwarded to the sketch.

Here the BLE stack of MBED will be set to initialize, _ble.init(), and once completed it will return to on_init_complete(). The AMDTPS protocol is initialize with _tp.amdtps_init() and a call back to the protocol is set back to Data_From_AMDTP when received data has been processed.
Now the event_queue is started (_event_queue.dispatch_forever();) and the BLE_init is handled

Start_discovery()
Is called when the client has connected to the server, it will start the discovery process of the services, characteristic and descriptors. Only if the service is equal to the AMDTP service UUID the data for the characteristics and descriptors will be looked up and stored. During the process it will also describe to the notify handlers. Once the discovery process is over a check will be done that all the needed characteristics the AMDTP protocol will be initialize and the _DiscoverySuccess – flag is set.

when_characteristic_changed()at is received will be passed on the AMDTP protocol AmdtpReceivePkt()

Data_From_AMDTP()
This callback was set during Start() and any complete received / processed data-packet coming from the protocol handling is passed back to the sketch StoreDataReceived()

SendToServer()
This routine will pass the request to sent data to the protocol handling with AmdtpSendData(). When the processed data-packet is less than the default MTU size ( 23 – 3 = 20 bytes) it can be send within on AMDTP packet and complete in one transaction. The maximum raw data packet is then max 12 bytes ( 8 byte overhead on first packet). If it needs to send multiple packages a time is set to prevent a deadlock. Next to that the sketch can call IsSendingComplete() to detect whether the AMDTP transaction has been completed.

IsSendingComplete()
Can be called to check that sending has been completed in case off multi chunks needed to be sent.

## amdtpc_protocol

amdtps_init()
This is called from start in gatt_server_amdtp. It will set different pointers and buffers to the start position.

AmdtpReceivePkt()
This is called from when_characteristic_changed() in gatt_client_amdtp. When the first AMDTP packet is received it will contain a length field (16 bits) and header (16 bits). The length field is the sum of all the data that should arrive + 4 byte CRC. The packet can either be a real data packet for the sketch program or internal ACK or control package. These will be stored in different buffers.
As it receives the length and header data is stored. The rest of the received data is stored in the selected buffer. When the next AMDTP packet all the received data is added into the buffer, until the complete length has been received. The last 4 bytes in the receive buffer are the CRC32 bytes. A CRC-32 calculation is performed over the buffer in the receive buffer (minus the last 4 bytes). If that calculated CRC matches the received CRC-bytes the packet has been received successful. An ACK will be send to the sender to indicate successful. completion. Now the received data is passed on to AmdtpPacketHandler()

******************************************************************************
NOTE 2: If the complete data has not been completed an extra step had to be added.
The sending from server/peripheral is happening on a notify characteristic. We can send very quickly on that, but the client/central side it needs to be able to keep up with that speed with enough buffers. That is often NOT the case if you send 26 packet ( 512 /20) very fast and package are dropped on the receiving side.

Hence I have implemented that after each 20 byte (or MTU size) packet has been sent the sending side (either client/central or server/peripheral) will wait for the other side to confirm it has received this packet. Only after that it will send the next chunk / packet. This is indicated in the header with setting the ACK-bit and only needed for sketch data-packages. Not for internal ACK or Control.

The result is that all the packets are received, BUT each packet will take a turn-around time of 375ms. Measured between Artemis Edge and Artemis ATP board. Thus sending 512 bytes will take 10s on an a default MTU size.

When connecting to BLEAK (on Ubuntu) the 512 bytes takes 3 seconds. MUCH faster, but still
3000 / 512 = 6ms per byte = 1000 / 6 = 160 bytes per second.

Not fast... but for many sensor this speed will be acceptable as most produce only a small amount of bytes.

*******************************************************************************

AmdtpPacketHandler()
It will check whether the package is data for the sketch and if so it will call the stored call back function ( Data_From_AMDTP ) as set in start in gatt_client_amdtp.
The package also be an ACK in reaction on previous sent data. The status is checked to see whether it was successful. or failed.

The package can also be a CONTROL package. One of the control request AMDTP_CONTROL_SEND_READY, meaning start sending the next AMDTP package. (see note 2)

AmdtpSendData()
Is called from SendToServer in gatt_client_amdtp. It will call AmdtpsSendPacket() with the type of packet to send .
In AmdtpsSendPacket() it will perform some checks and it will then call AmdtpBuildPkt() to create the AMDTP packet to be send. As a last point it will call AmdtpSendPacketHandler(0 to perform sending the packet in chunks

AmdtpBuildPkt()
Here the AMDTP is build. It will add the length and the header. If the length (including overhead bytes) is longer than the MTUsize – 3 (most of the time 23 3 = 20 bytes), it will set the ACK-bit in the header to indicate that after each packet an confirmation is required. It copies the data to send and the CRC-32 to the packet

AmdtpSendPacketHandler()
This routine can be called multiple times. The first time it will initialize and then send the first packet. If sending the complete package takes multiple chunk of 20 bytes, it will wait until is called again from AmdtpPacketHandler() as the control package was received from the other side indicating the previous chunk had arrived. If the complete package has been send, it will indicate that it is done with sending and now waiting on an ACK from the receiver that the CRC-32 was correct.

AmdtpSendComplete()
This is called from IsSendingComplete() it will check with the flag is set or cleared that the complete package in chunks was send.

# Debug

There are multiple ways to set debug.
In the sketch you can set a debug flag. This will enable MBED debug messages. Make sure to read the SetDebugBLE.txt file in the library on how to set the different debug messages in MBED. It might need recompile of the MBED archive, but that is all explained.

At the top on nearly all header files you can enable debug messages for the header and associated cpp file. This will requires recompile of the sketch.